## Slide 1: EE 315/ECE 451 Nanoelectronics I
Ch 5 Electrons Subject to a Periodic Potential – Band Theory of Solids
Adapted from a lecture by Dr. Ryan Munden

## Slide 2: Outline
5.1 Crystalline Materials
5.2 Electrons in a Periodic Potential
5.3 Kronig-Penny Model of Band Structure
5.4 Band Theory of Solids
5.5 Graphene and Carbon Nanotubes
5.6 Main Points

## Slide 3: 5.4 Band Theory of Solids
Notes: e - Work Function – the energy difference between the vacuum level and the Fermi level – the energy needed to liberate an electron from the metal at absolute zero

## Slide 4: Photoelectric Effect
Photons with energy greater than the work function can liberate the electrons from a metal

## Slide 5: Insulator Band Structure
Notes: Eg – energy required to raise an electron to a conduction band.

## Slide 6: Semicondcutor Band Structure
Don’t forget the holes!
Notes: Eg is smaller for a semiconductor (~1.2-1.4 ev) than for an insulator (8-10 ev)

## Slide 7: Doping
Notes: Type n silicon extra free electrons

## Slide 8: Donors
These are n-type semiconductors

## Slide 9: Acceptors
These are p-type semiconductors
Notes: Extra holes – type P silicon - The Type is determined by the “majority” carrier – holes are “heavier” than electrons (effective mass). – They are less mobile.

## Slide 10: Interacting Systems Model
Notes: Splitting is due to the overlap of each system’s wavefunction.

## Slide 11: Atomic Bonding

## Slide 12: Atomic Development of Bands

## Slide 13: Electric Fields
Notes: Positive voltage pushes the energy level down – electrons will tend to “roll” downhill

## Slide 14: Direct Bandgap Semiconductors
Notes: e.g. GaAs, InP – the bottom of the conduction band is at k-0

## Slide 15: Indirect Bandgap Semiconductors

## Slide 16: Electron and Hole Energy

## Slide 17: Optical Transitions – Direct Gap
For T1
Notes: e.g. Si, Ge, AlAs – k > 0

## Slide 18: Optical Transitions – Indirect Gap

## Slide 19: Excitons
Notes: Exitron – a “bonded” hole-electron pair – easily broken apart by thermal energy into free electrons and holes

## Slide 20: Low-Temperature Effects

## Slide 21: 5.5 Graphene
Notes: A flat, one molecule thick, crystalline sheet of carbon – a two dimensional structur

## Slide 22: Graphene Unit Cell

## Slide 23: Graphene Bands

## Slide 24: Carbon Nanotubes
3 types: zigzag, armchair, and chiral tubes
Notes: Wrap a graphene sheet into a tube – occurs naturally in an arc discharge of carbon electrodes.

## Slide 25: Chirality

## Slide 26: Nanotubes
Zigzag, armchair and chiral where
Are metallic, otherwise semiconducting
Where the bandgap is:
Notes: 3 types depending on the symmetry reqired to “close” the tube.

## Slide 27: 4.8 Problems