## Slide 1
ADDITIONAL ANALYSIS TECHNIQUES
LEARNING GOALS
REVIEW LINEARITY
The property has two equivalent definitions.
We show and application of homogeneity
APPLY SUPERPOSITION
We discuss some implications of the superposition property in
linear circuits
DEVELOP THEVENIN’S AND NORTON’S THEOREMS
These are two very powerful analysis tools that allow us to
focus on parts of a circuit and hide away unnecessary complexities
MAXIMUM POWER TRANSFER
This is a very useful application of Thevenin’s and Norton’s theorems

## Slide 2
    The techniques developed in chapter 2; i.e., combination series/parallel,
    voltage divider and current divider are special techniques that are more
    efficient than the general methods, but have a limited applicability.
    It is to our advantage to keep them in our repertoire and use them when
    they are more efficient.
In this section we develop additional techniques that simplify
the analysis of some circuits.
In fact these techniques expand on concepts that we have
already introduced: linearity and circuit equivalence
THE METHODS OF NODE AND LOOP ANALYSIS PROVIDE POWERFUL TOOLS TO
DETERMINE THE BEHAVIOR OF EVERY COMPONENT IN A CIRCUIT

## Slide 3
SOME EQUIVALENT CIRCUITS
ALREADY USED

## Slide 4
LINEARITY
THE MODELS USED ARE ALL LINEAR.
MATHEMATICALLY THIS IMPLIES THAT THEY
SATISFY THE PRINCIPLE OF SUPERPOSITION
AN ALTERNATIVE, AND EQUIVALENT,
DEFINITION OF LINEARITY SPLITS THE
SUPERPOSITION PRINCIPLE IN TWO.
NOTICE THAT, TECHNICALLY, LINEARITY CAN
NEVER BE VERIFIED EMPIRICALLY ON A SYSTEM.
BUT IT COULD BE DISPROVED BY A SINGLE
COUNTER EXAMPLE.
IT CAN BE VERIFIED MATHEMATICALLY FOR THE
MODELS USED.
USING NODE ANALYSIS FOR RESISTIVE
CIRCUITS ONE OBTAINS MODELS OF THE
FORM
v IS A VECTOR CONTAINING ALL THE NODE
VOLTAGES AND f IS A VECTOR DEPENDING
ONLY ON THE INDEPENDENT SOURCES.
IN FACT THE MODEL CAN BE MADE MORE
DETAILED AS FOLLOWS
HERE, A,B, ARE MATRICES AND s IS A VECTOR
OF ALL INDEPENDENT SOURCES
FOR CIRCUIT ANALYSIS WE CAN USE THE
LINEARITY ASSUMPTION TO DEVELOP
SPECIAL ANALYSIS TECHNIQUES
FIRST WE REVIEW THE TECHNIQUES
CURRENTLY AVAILABLE

## Slide 5
A CASE STUDY TO REVIEW PAST TECHNIQUES
Redrawing the circuit may help us
in recognizing special cases
SOLUTION TECHNIQUES AVAILABLE??

## Slide 7
USING HOMOGENEITY
Assume that the answer is known. Can we
Compute the input in a very easy way ?!!
If Vo is given then V1 can be computed
using an inverse voltage divider.
… And Vs using a second voltage divider
Solve now for the variable Vo
The procedure can be made entirely algorithmic
1. Give to Vo any arbitrary value (e.g., V’o =1 )
2. Compute the resulting source value and call it V’_s
3. Use linearity.
4. The given value of the source (V_s)
corresponds to
Hence the desired output value is
This is a nice little tool
for special problems.
Normally when there is
only one source and
when in our judgement
solving the problem
backwards is actually
easier

## Slide 8
SOLVE USING HOMOGENEITY
NOW USE HOMOGENEITY

## Slide 9
LEARNING EXTENSION

## Slide 10
Source Superposition
This technique is a direct application of
linearity.
It is normally useful when the circuit has only
a few sources.

## Slide 11
Due to Linearity
Can be computed by setting the current
source to zero and solving the circuit
Can be computed by setting the voltage
source to zero and solving the circuit
FOR CLARITY WE SHOW A CIRCUIT
WITH ONLY TWO SOURCES

## Slide 12
Circuit with current
source set to zero(OPEN)
Circuit with voltage source
set to zero (SHORT CIRCUITED)
SOURCE SUPERPOSITION
=
+
The approach will be useful if solving the two circuits is simpler, or more convenient, than
solving a circuit with two sources
Due to the linearity of the models we must have
Principle of Source Superposition
We can have any combination of sources. And we can partition any way we find convenient

## Slide 13
LEARNING EXAMPLE
=
+
Loop equations
Contribution of v1
Contribution of v2
WE WISH TO COMPUTE THE CURRENT
Once we know the “partial circuits”
we need to be able to solve them in
an efficient manner

## Slide 14
LEARNING EXAMPLE
We set to zero the voltage source
Current division
Ohm’s law
Now we set to zero the current source
Voltage Divider

## Slide 15
LEARNING EXAMPLE
Set to zero voltage source
We must be able to solve each circuit in a very
efficient manner!!!
Set to zero current source
If V1 is known then V’o is obtained using a voltage divider
V1 can be obtained by series parallel reduction and divider
The current I2 can be obtained using a current divider
and V”o using Ohm’s law
WHEN IN DOUBT… REDRAW!

## Slide 16
Sample Problem
1. Consider only the voltage source
3. Consider only the 4mA source
2. Consider only the 3mA
source
Current divider
Using source superposition

## Slide 17
1
1
2
2
3
3
Linearity