## Slide 1
These are some of the most powerful analysis results to be discussed.
They permit to hide information that is not relevant and concentrate in what is important to the analysis
THEVENIN’S AND NORTON’S THEOREMS

## Slide 2
http://angelfire.com/ab3/mjramp/index.html
Low distortion audio power amplifier
From PreAmp
(voltage )
To speakers
TO MATCH SPEAKERS AND AMPLIFIER
IT IS MUCH EASIER TO CONSIDER THIS
EQUIVALENT CIRCUIT!
TO MATCH SPEAKERS AND
AMPLIFIER ONE SHOULD ANALYZE
THIS CIRCUIT
REPLACE AMPLIFIER
BY SIMPLER
“EQUIVALENT”
Courtesy of M.J. Renardson

## Slide 3
THEVENIN’S EQUIVALENCE THEOREM
Thevenin Equivalent Circuit
for PART A

## Slide 4
NORTON’S EQUIVALENCE THEOREM
Norton Equivalent Circuit
for PART A

## Slide 5
Examples of Valid and Invalid Partitions

## Slide 6
OUTLINE OF PROOF - version 1
If Circuit A is unchanged then the current should be the same FOR ANY Vo
USE SOURCE SUPERPOSITION
All independent
sources set to
zero in A
HOW DO WE INTERPRET THIS RESULT?

## Slide 7
OUTLINE OF PROOF - version 2
2. Result must hold for “every valid Part B” that we can imagine
1. Because of the linearity of the models, for any Part B the relationship
between Vo and the current, i, has to be of the form
3. If part B is an open circuit then i=0 and...
4. If Part B is a short circuit then Vo is zero. In this case
How do we interpret this?

## Slide 8
This is the Thevenin equivalent
circuit for the circuit in Part A
For ANY circuit in Part B
The voltage source is called the
THEVENIN EQUIVALENT SOURCE
The resistance is called the
THEVENIN EQUIVALENT RESISTANCE
PART A MUST BEHAVE LIKE
THIS CIRCUIT
THEVENIN APPROACH

## Slide 9
Norton Approach
Norton

## Slide 10
Thevenin
This equivalence can be viewed as a source transformation problem
It shows how to convert a voltage source in series with a resistor
into an equivalent current source in parallel with the resistor
Norton
ANOTHER VIEW OF THEVENIN’S AND NORTON’S THEOREMS
SOURCE TRANSFORMATION CAN BE A GOOD TOOL TO REDUCE THE
COMPLEXITY OF A CIRCUIT

## Slide 11
Source transformation is a good tool to reduce complexity in a circuit ...
WHEN IT CAN BE APPLIED!!
Source Transformationcan be used to determine the Thevenin or Norton Equivalent...
BUT THERE MAY BE MORE EFFICIENT TECHNIQUES
“ideal sources” are not good models for real behavior of sources
A real battery does not produce infinite current when short-circuited

## Slide 12
EXAMPLE: SOLVE BY SOURCE TRANSFORMATION
The equivalent current source will have the
value 12V/3k
The 3k and the 6k resistors now are in parallel
and can be combined
In between the terminals we connect a current
source and a resistance in parallel
In between the terminals we connect a voltage
source in series with the resistor
The equivalent source has value 4mA*2k
The 2k and the 2k resistor become connected
in series and can be combined
After the transformation the sources can be combined
The equivalent current source has value 8V/4k
and the combined current source has value 4mA
Options at this point
1. Do another source transformation and get
a single loop circuit
2. Use current divider to compute I_0 and then
compute V_0 using Ohm’s law

## Slide 13
Or one more source transformation
PROBLEM Compute V_0 using source transformation
3 current sources in parallel and
three resistors in parallel
EQUIVALENT CIRCUITS

## Slide 14
Source Transformationcan be used to determine the Thevenin or Norton Equivalent...
WE NOW REVIEW SEVERAL EFFICIENT APPROACHES
TO DETERMINE THEVENIN OR NORTON EQUIVALENT
CIRCUITS
RECAP OF SOURCE TRANSFORMATION

## Slide 15
A General Procedure to Determine the Thevenin Equivalent
1. Determine the
Thevenin equivalent
source
Remove part B and
compute the OPEN
CIRCUIT voltage
2. Determine the
SHORT CIRCUIT
current
Remove part B and
compute the SHORT
CIRCUIT current
Second circuit problem
One circuit problem

## Slide 16
AN EXAMPLE OF DETERMINING THE THEVENIN EQUIVALENT
Part B is irrelevant.
The voltage V_ab will be the value of the
Thevenin equivalent source.
What is an efficient technique to compute the
open circuit voltage?
Now for the short circuit current
Lets try source superposition
When the current source is open the
current through the short circuit is
When the voltage source is set to zero,
the current through the short circuit is
To compute the Thevenin resistance we
use
For this case the Thevenin resistance can be computed as
the resistance from a - b when all independent sources have been
set to zero
Is this a
general
result?
NODE
ANALYSIS

## Slide 17
Determining the Thevenin Equivalent in Circuits with Only INDEPENDENT SOURCES
The Thevenin Equivalent Source is computed as the open loop voltage
The Thevenin Equivalent Resistance CAN BE COMPUTED by setting to zero all the sources
and then determining the resistance seen from the terminals where the equivalent will be placed
“Part B”
“Part B”
Since the evaluation of the Thevenin
equivalent can be very simple, we
can add it to our toolkit for the
solution of circuits!!

## Slide 18
“PART B”
LEARNING BY DOING

## Slide 19
LEARNING EXAMPLE
In the region shown, one could use source
transformation twice and reduce that part to
a single source with a resistor.
... Or we can apply Thevenin Equivalence
to that part (viewed as “Part A”)
For the open loop voltage
the part outside the region
is eliminated
The original circuit becomes...
And one can apply Thevenin one more time!
For open loop voltage use KVL
...and we have a simple voltage divider!!
COMPUTE Vo USING THEVENIN

## Slide 20
Or we can use Thevenin only once to get a voltage divider
“Part B”
For the Thevenin resistance
For the Thevenin voltage we have to analyze the
following circuit
METHOD??
Source superposition, for example
Contribution of the voltage source
Contribution of the current source
Simple Voltage Divider
Thevenin Equivalent of “Part A”

## Slide 21
LEARNING EXAMPLE
You have the choice on the way to partition
the circuit.
Make “Part A” as simple as possible
“Part B”
Since there are only independent sources,
for the Thevenin resistance we set to zero all
sources and determine the equivalent resistance
For the open circuit voltage we analyze the
following circuit (“Part A”) ...
The circuit becomes...
USE THEVENIN TO COMPUTE Vo

## Slide 22
LEARNING EXTENSION: USE THEVENIN TO COMPUTE Vo
“PART B”
RESULTING EQUIVALENT CIRCUIT

## Slide 23
LEARNING EXTENSION: COMPUTE Vo USING NORTON
PART B
COMPUTE Vo USING THEVENIN
PART B

## Slide 24
SAMPLE PROBLEM
This is what we need to get
Equivalent Resistance: Independent sources only
Equivalent Voltage: Node, loop, superposition…
KVL
How about source superposition?
Opening the current source:
Short circuiting the voltage source
KVL
Do loops

## Slide 25
SAMPLE PROLEM
All independent sources
All resistors are in parallel!!
The circuit can be simplified
,,, An to compute Equivalent Source...
Voltage divider
SOURCE
TRANSFORMATION

## Slide 26
THEVENIN EQUIVALENT FOR CIRCUITS WITH ONLY DEPENDENT SOURCES
A circuit with only dependent sources cannot self start.
This is a big simplification!!
But we need a special approach for the
computation of the Thevenin equivalent resistance
Since the circuit cannot self start we need to probe it
with an external source
The source can be either a voltage source or a
current source and its value can be chosen arbitrarily!
Which one to choose is often determined by the
simplicity of the resulting circuit
(actually that statement has to be qualified a bit.
What happens if )
FOR ANY PROPERLY DESIGNED CICUIT WITH ONLY DEPENDENT
SOURCES

## Slide 27
IF WE CHOOSE A VOLTAGE PROBE...
The value chosen for the probe voltage is irrelevant.
Oftentimes we simply set it to one
WE MUST COMPUTE CURRENT SUPPLIED BY
PROBE SOURCE

## Slide 28
IF WE CHOOSE A CURRENT SOURCE PROBE
We must compute the node voltage V_p
The value of the probe current is irrelevant. For simplicity
it is often choosen as one.

## Slide 29
LEARNING EXAMPLE
Do we use current probe or voltage probe?
Controlling variable:
If we use voltage probe there is only one
node not connected through source
Using voltage probe. Must compute
current supplied
FIND THE THEVENIN EQUIVALENT

## Slide 30
LEARNING EXAMPLE
Only dependent sources. Hence V_th = 0
To compute the equivalent resistance we
must apply an external probe
We choose to apply a current probe
@V_1
@V_2
Controlling variable
“Conventional” circuit with dependent
sources - use node analysis
Thevenin equivalent
Find the Thevenin Equivalent circuit at A - B

## Slide 31
SAMPLE PROBLEM
Loop analysis
Controlling variable
Voltage across current probe
Thevenin equivalent
The resistance is
numerically equal
to V_p but with
units of KOhm

## Slide 32: Thevenin Equivalent Circuits with both Dependent and Independent Sources
We will compute open circuit voltage and short circuit current
For each determination of a Thevenin equivalent
we will solve two circuits
Any and all the techniques discussed should be readily
available; e.g.,
KCL, KVL,combination series/parallel, node, loop analysis,
source superposition, source transformation, homogeneity
The approach of setting to zero all sources and then
combining resistances to determine the Thevenin
resistance is in general not applicable!!

## Slide 33
EXAMPLE Use Thevenin to determine Vo
“Part B”
“Part A” should be as simple as possible.
After “Part A” is replaced by the Thevenin
equivalent we should have a very simple circuit
Guidelines to partition:
Open circuit voltage
The dependent sources and their controlling
variables must remain together
Options???
Constraint at super node
KCL at super node
Equation for controlling variable
Solve
Short circuit current
Setting all sources to zero and combining
resistances will yield an incorrect value!!!!
Negative resistances for some “a’s”
Solution to the problem

## Slide 34
Find Vo using Thevenin
Open circuit voltage
Super node
Method???
KVL
Controlling variable
KVL
Short Circuit Current
KCL
The equivalent circuit
The equivalent resistance cannot be obtained by
short circuiting the sources and determining the
resistance of the resulting interconnection of resistors

## Slide 35
EXAMPLE: Use Thevenin to compute Vo
DON’T PANIC!!
Select your partition
“Part B”
Open Circuit Voltage
Loop equations
Controlling variable
Short circuit current
Loop equations
Controlling variable
Same as before
Thevenin resistance
Now compute V_0 using the Thevenin equivalent
KVL for V_oc
Use loops

## Slide 36
The alternative for mixed sources
Open circuit voltage
Short circuit current
Equivalent Resistance
EXAMPLE

## Slide 37
SAMPLE PROBLEM
Mixed sources. Must compute Voc and Isc
Open circuit voltage
KCL at super node
The two 4k resistors are in parallel
Short circuit current
KVL
FINAL ANSWER
supernode
KCL at supernode

## Slide 38
SAMPLE PROBLEM
Mixed sources! Must compute open loop voltage and
short circuit current
Open circuit voltage
For Vx use voltage divider
For Vb use KVL
Short circuit current
We need to compute V_x
Single node
KCL@Vx
KCL again can give the short circuit current
FINAL ANSWER

## Slide 39
LEARNING EXAMPLE
Using EXCEL to generate and plot data
DATA TO BE PLOTTED

## Slide 41
LEARNING EXAMPLE
Using MATLAB to generate and plot data
DATA TO BE PLOTTED
» Rx=[0:0.1:10]'; %define the range of resistors to use
» Voc=12-6*Rx./(Rx+4); %the formula for Voc. Notice "./"
» Rth=4*Rx./(4+Rx); %formula for Thevenin resistance.
» plot(Rx,Voc,'bo', Rx,Rth,'md')
» title('USING MATLAB'), %proper graphing tools
» grid, xlabel('Rx(kOhm)'), ylabel('Volts/kOhms')
» legend('Voc[V]','Rth[kOhm]')

## Slide 42
A MORE GENERAL VIEW OF THEVENIN THEOREM
THIS INTERPRETATION APPLIES
EVEN WHEN THE PASSIVE ELEMENTS
INCLUDE INDUCTORS AND CAPACITORS
USUAL INTERPRETATION
Thevenin

## Slide 43
MAXIMUM POWER TRANSFER
From PreAmp
(voltage )
To speakers
The simplest model for a
speaker is a resistance...
BASIC MODEL FOR THE
ANALYSIS OF POWER
TRANSFER
http://angelfire.com/ab3/mjramp/index.html
Courtesy of M.J. Renardson

## Slide 44
MAXIMUM POWER TRANSFER
For every choice of R_L we have a different power.
How do we find the maximum value?
Consider P_L as a function of R_L and find the
maximum of such function
3
Set the derivative to zero to find extreme points.
For this case we need to set to zero the numerator
The maximum
power transfer
theorem
The load that maximizes the power transfer for a circuit is
equal to the Thevenin equivalent resistance of the circuit.
Technically we need
to verify that it is
indeed a maximum
The value of the maximum
power that can be
transferred is
ONLY IN THIS CASE WE NEED TO COMPUTE THE THEVENIN VOLTAGE

## Slide 45
LEARNING EXAMPLE
a
b
We need to find the Thevenin resistance
at a - b.
The circuit contains only independent sources ....
Resistance for maximum
power transfer
If we MUST find the value of the
power that can be transferred THEN
we need the Thevenin voltage!!!

## Slide 46
LEARNING EXAMPLE
a
b
1. Find the Thevenin equivalent at a - b
2. Remember that for maximum power
transfer
This is a mixed sources problem
.... And it is simpler if we do Thevenin
at c - d and account for the 4k at the end
c
d
Controlling variable:
Now the short circuit current
Remember now where the partition was made