## Slide 1
Variable-Frequency Response Analysis
Network performance as function of frequency.
Transfer function
Sinusoidal Frequency Analysis
Bode plots to display frequency response data
Resonant Circuits
The resonance phenomenon and its characterization
Scaling
Impedance and frequency scaling
Filter Networks
Networks with frequency selective characteristics:
low-pass, high-pass, band-pass
VARIABLE-FREQUENCY NETWORK
PERFORMANCE
LEARNING GOALS

## Slide 2
Resistor
VARIABLE FREQUENCY-RESPONSE ANALYSIS
In AC steady state analysis the frequency is assumed constant (e.g., 60Hz).
Here we consider the frequency as a variable and examine how the performance
varies with the frequency.
Variation in impedance of basic components

## Slide 3
Inductor

## Slide 4
Capacitor

## Slide 5
Frequency dependent behavior of series RLC network

## Slide 6
For all cases seen, and all cases to be studied, the impedance is of the form
Simplified notation for basic components
Moreover, if the circuit elements (L,R,C, dependent sources) are real then the
expression for any voltage or current will also be a rational function in s
LEARNING EXAMPLE
MATLAB can be effectively used to compute frequency response characteristics

## Slide 7
USING MATLAB TO COMPUTE MAGNITUDE AND PHASE INFORMATION
MATLAB commands required to display magnitude
and phase as function of frequency
NOTE: Instead of comma (,) one can use space to
separate numbers in the array
EXAMPLE
» num=[15*2.53*1e-3,0];
» den=[0.1*2.53*1e-3,15*2.53*1e-3,1];
» freqs(num,den)
Missing coefficients must
be entered as zeros
» num=[15*2.53*1e-3 0];
» den=[0.1*2.53*1e-3 15*2.53*1e-3 1];
» freqs(num,den)
This sequence will also
work. Must be careful not
to insert blanks elsewhere

## Slide 8
GRAPHIC OUTPUT PRODUCED BY MATLAB
Log-log
plot
Semi-log
plot

## Slide 9
LEARNING EXAMPLE
A possible stereo amplifier
Desired frequency characteristic
(flat between 50Hz and 15KHz)
Postulated amplifier
Log frequency scale

## Slide 10
Frequency domain equivalent circuit
Frequency Analysis of Amplifier
required
actual
Frequency dependent behavior is
caused by reactive elements
Voltage Gain

## Slide 11
NETWORK FUNCTIONS
When voltages and currents are defined at different terminal pairs we
define the ratios as Transfer Functions
If voltage and current are defined at the same terminals we define
Driving Point Impedance/Admittance
Some nomenclature
EXAMPLE
To compute the transfer functions one must solve
the circuit. Any valid technique is acceptable

## Slide 12
LEARNING EXAMPLE
The textbook uses mesh analysis. We will
use Thevenin’s theorem

## Slide 13
POLES AND ZEROS
(More nomenclature)
Arbitrary network function
Using the roots, every (monic) polynomial can be expressed as a
product of first order terms
The network function is uniquely determined by its poles and zeros
and its value at some other value of s (to compute the gain)
EXAMPLE

## Slide 14
LEARNING EXTENSION
Find the driving point impedance at
Replace numerical values

## Slide 15
LEARNING EXTENSION
For this case the gain was shown to be
Zeros = roots of numerator
Poles = roots of denominator
Variable
Frequency
Response

## Slide 16
SINUSOIDAL FREQUENCY ANALYSIS
Circuit represented by
network function

## Slide 17
HISTORY OF THE DECIBEL
Originated as a measure of relative (radio) power
By extension
Using log scales the frequency characteristics of network functions
have simple asymptotic behavior.
The asymptotes can be used as reasonable and efficient approximations

## Slide 18
General form of a network function showing basic terms
Frequency independent
Poles/zeros at the origin
First order terms
Quadratic terms for
complex conjugate poles/zeros
Display each basic term
separately and add the
results to obtain final
answer
Let’s examine each basic term

## Slide 19
Constant Term
Poles/Zeros at the origin

## Slide 20
Simple pole or zero
Behavior in the neighborhood of the corner
Asymptote for phase
High freq. asymptote
Low freq. Asym.

## Slide 21
Simple zero
Simple pole

## Slide 22
Quadratic pole or zero
Corner/break frequency
Resonance frequency
Magnitude for quadratic pole
Phase for quadratic pole
These graphs are inverted for a zero

## Slide 23
LEARNING EXAMPLE
Generate magnitude and phase plots
Draw asymptotes
for each term
Draw composites

## Slide 24
asymptotes

## Slide 25
LEARNING EXAMPLE
Generate magnitude and phase plots
Draw asymptotes for each
Form composites

## Slide 26
Final results . . . And an extra hint on poles at the origin

## Slide 27
LEARNING EXTENSION
Sketch the magnitude characteristic
Put in standard form
We need to show about
4 decades

## Slide 28
LEARNING EXTENSION
Sketch the magnitude characteristic
Once each term is drawn we form the composites

## Slide 29
Put in standard form
LEARNING EXTENSION
Sketch the magnitude characteristic
Once each term is drawn we form the composites

## Slide 30
LEARNING EXAMPLE
A function with complex conjugate poles
Put in standard form
Draw composite asymptote
Behavior close to corner of conjugate pole/zero
is too dependent on damping ratio.
Computer evaluation is better

## Slide 31
Evaluation of frequency response using MATLAB
» num=[25,0]; %define numerator polynomial
» den=conv([1,0.5],[1,4,100]) %use CONV for polynomial multiplication
den =
1.0000 4.5000 102.0000 50.0000
» freqs(num,den)
Using default options

## Slide 32
Evaluation of frequency response using MATLAB
User controlled
>> clear all; close all %clear workspace and close any open figure
>> figure(1) %open one figure window (not STRICTLY necessary)
>> w=logspace(-1,3,200);%define x-axis, [10^{-1} - 10^3], 200pts total
>> G=25*j*w./((j*w+0.5).*((j*w).^2+4*j*w+100)); %compute transfer function
>> subplot(211) %divide figure in two. This is top part
>> semilogx(w,20*log10(abs(G))); %put magnitude here
>> grid %put a grid and give proper title and labels
>> ylabel('|G(j\omega)|(dB)'), title('Bode Plot: Magnitude response')

## Slide 33
>> semilogx(w,unwrap(angle(G)*180/pi)) %unwrap avoids jumps from +180 to -180
>> grid, ylabel('Angle H(j\omega)(\circ)'), xlabel('\omega (rad/s)')
>> title('Bode Plot: Phase Response')
Evaluation of frequency response using MATLAB
User controlled
Continued
Repeat for phase
No xlabel here to avoid clutter
USE TO ZOOM IN A SPECIFIC REGION OF INTEREST
Compare with default!

## Slide 34
LEARNING EXTENSION
Sketch the magnitude characteristic

## Slide 35
» num=0.2*[1,1];
» den=conv([1,0],[1/144,1/36,1]);
» freqs(num,den)

## Slide 36
DETERMINING THE TRANSFER FUNCTION FROM THE BODE PLOT
This is the inverse problem of determining frequency characteristics.
We will use only the composite asymptotes plot of the magnitude to postulate
a transfer function. The slopes will provide information on the order
A
A. different from 0dB.
There is a constant Ko
B
B. Simple pole at 0.1
C
C. Simple zero at 0.5
D
D. Simple pole at 3
E
E. Simple pole at 20
If the slope is -40dB we assume double real pole. Unless we are given more data

## Slide 37
LEARNING EXTENSION
Determine a transfer function from the composite
magnitude asymptotes plot
A
A. Pole at the origin.
Crosses 0dB line at 5
B
B. Zero at 5
C
C. Pole at 20
D
D. Zero at 50
E
E. Pole at 100
Sinusoidal

## Slide 38
RESONANT CIRCUITS - SERIES RESONANCE
RESONANT FREQUENCY
PHASOR DIAGRAM
QUALITY FACTOR

## Slide 39
RESONANT CIRCUITS
These are circuits with very special frequency characteristics…
And resonance is a very important physical phenomenon
The frequency at which the circuit becomes purely resistive is called
the resonance frequency

## Slide 40
Properties of resonant circuits
At resonance the impedance/admittance is minimal
Current through the serial circuit/
voltage across the parallel circuit can
become very large (if resistance is small)
Given the similarities between series and parallel resonant circuits,
we will focus on serial circuits

## Slide 41
Properties of resonant circuits
At resonance the power factor is unity
Phasor diagram for series circuit
Phasor diagram for parallel circuit

## Slide 42
LEARNING EXAMPLE
Determine the resonant frequency, the voltage across each
element at resonance and the value of the quality factor

## Slide 43
LEARNING EXAMPLE
Given L = 0.02H with a Q factor of 200, determine the capacitor
necessary to form a circuit resonant at 1000Hz
What is the rating for the capacitor if the
circuit is tested with a 10V supply?
The reactive power on the capacitor
exceeds 12kVA

## Slide 44
LEARNING EXTENSION
Find the value of C that will place the circuit in resonance
at 1800rad/sec
Find the Q for the network and the magnitude of the voltage across the
capacitor

## Slide 45
Resonance for the series circuit

## Slide 46
The Q factor
dissipates
Stores as E
field
Stores as M
field
Capacitor and inductor exchange stored
energy. When one is at maximum the
other is at zero
Q can also be interpreted from an
energy point of view

## Slide 47
ENERGY TRANSFER IN RESONANT CIRCUITS
Normalization
factor

## Slide 48
LEARNING EXAMPLE
Determine the resonant frequency, quality factor and
bandwidth when R=2 and when R=0.2
Evaluated with EXCEL

## Slide 49
LEARNING EXTENSION
A series RLC circuit as the following properties:
Determine the values of L,C.
1. Given resonant frequency and bandwidth determine Q.
2. Given R, resonant frequency and Q determine L, C.

## Slide 50
LEARNING EXAMPLE
Find R, L, C so that the circuit operates as a band-pass filter
with center frequency of 1000rad/s and bandwidth of 100rad/s
dependent
Strategy:
1. Determine Q
2. Use value of resonant frequency and Q to set up two equations in the three
unknowns
3. Assign a value to one of the unknowns
For example

## Slide 51
PROPERTIES OF RESONANT CIRCUITS: VOLTAGE ACROSS CAPACITOR
But this is NOT the maximum value for the
voltage across the capacitor

## Slide 52
LEARNING EXAMPLE
Natural frequency depends only on L, C.
Resonant frequency depends on Q.
Evaluated with EXCEL and rounded to zero decimals
Using MATLAB one can display the frequency response

## Slide 53
R=50
Low Q
Poor selectivity
R=1
High Q
Good selectivity

## Slide 54
LEARNING EXAMPLE
The Tacoma Narrows Bridge
Opened: July 1, 1940
Collapsed: Nov 7, 1940
Likely cause: wind
varying at frequency
similar to bridge
natural frequency

## Slide 55
Tacoma Narrows Bridge Simulator
Assume a low Q=2.39
0.44’
1.07’

## Slide 56
PARALLEL RLC RESONANT CIRCUITS
Impedance of series RLC
Admittance of parallel RLC
Series RLC
Parallel RLC
Series RLC
Parallel RLC

## Slide 57
VARIATION OF IMPEDANCE AND PHASOR DIAGRAM – PARALLEL CIRCUIT

## Slide 58
LEARNING EXAMPLE
If the source operates at the resonant frequency of the
network, compute all the branch currents

## Slide 59
LEARNING EXAMPLE
Derive expressions for the resonant frequency, half power
frequencies, bandwidth and quality factor for the transfer
characteristic
Replace and show

## Slide 60
LEARNING EXAMPLE
Increasing selectivity by cascading low Q circuits
Single stage tuned amplifier

## Slide 61
LEARNING EXTENSION
Determine the resonant frequency, Q factor and bandwidth
Parallel RLC

## Slide 62
LEARNING EXTENSION
Parallel RLC
Can be used to verify computations

## Slide 63
PRACTICAL RESONANT CIRCUIT
The resistance of the inductor coils cannot be
neglected
How do you define a quality factor for
this circuit?

## Slide 64
LEARNING EXAMPLE

## Slide 65
RESONANCE IN A MORE GENERAL VIEW
For series connection the impedance reaches maximum at resonance. For parallel
connection the impedance reaches maximum
A high Q circuit is highly
under damped
Resonance

## Slide 66
SCALING
Scaling techniques are used to change an idealized network into a more
realistic one or to adjust the values of the components
Magnitude scaling does not change the
frequency characteristics nor the quality
of the network.
Constant Q
networks

## Slide 67
LEARNING EXAMPLE
Determine the value of the elements and the characterisitcs
of the network if the circuit is magnitude scaled by 100 and
frequency scaled by 1,000,000

## Slide 68
LEARNING EXTENSION
Scaling

## Slide 69
FILTER NETWORKS
Networks designed to have frequency selective behavior
COMMON FILTERS
Low-pass filter
High-pass filter
Band-pass filter
Band-reject filter
We focus first on
PASSIVE filters

## Slide 70
Simple low-pass filter

## Slide 71
Simple high-pass filter

## Slide 72
Simple band-pass filter
Band-pass

## Slide 73
Simple band-reject filter

## Slide 74
LEARNING EXAMPLE
Depending on where the output is taken, this circuit
can produce low-pass, high-pass or band-pass or band-
reject filters
Band-pass
Band-reject filter
High-pass
Low-pass

## Slide 75
LEARNING EXAMPLE
A simple notch filter to eliminate 60Hz interference

## Slide 76
LEARNING EXTENSION

## Slide 77
LEARNING EXTENSION

## Slide 78
LEARNING EXTENSION
Band-pass

## Slide 79
ACTIVE FILTERS
Passive filters have several limitations
1. Cannot generate gains greater than one
2. Loading effect makes them difficult to interconnect
3. Use of inductance makes them difficult to handle
Using operational amplifiers one can design all basic filters, and more,
with only resistors and capacitors
The linear models developed for operational amplifiers circuits are valid, in a
more general framework, if one replaces the resistors by impedances
Ideal Op-Amp
These currents are
zero

## Slide 80
Basic Inverting Amplifier
Linear circuit equivalent

## Slide 81
Basic Non-inverting amplifier
Basic Non-inverting Amplifier
Due to the internal op-amp circuitry, it has
limitations, e.g., for high frequency and/or
low voltage situations. The Operational
Transductance Amplifier (OTA) performs
well in those situations

## Slide 82
Operational Transductance Amplifier (OTA)
COMPARISON BETWEEN OP-AMPS AND OTAs – PHYSICAL CONSTRUCTION
Comparison of Op-Amp and OTA - Parameters

## Slide 83
Basic Op-Amp Circuit
Basic OTA Circuit

## Slide 84
Basic OTA Circuits
In the frequency domain

## Slide 85
Basic OTA Adder
Equivalent representation
OTA APPLICATION

## Slide 86
Controlling transconductance

## Slide 87
LEARNING EXAMPLE

## Slide 88
LEARNING EXAMPLE
Floating simulated resistor
One grounded terminal
The resistor cannot be produced
with this OTA!

## Slide 89
LEARNING EXAMPLE
Case a
Two equations in three unknowns.
Select one transductance
Case b
Reverse polarity of v2!

## Slide 90
ANALOG MULTIPLIER
ASSUMES VG IS ZERO
Based on ‘modulating the control current

## Slide 91
AUTOMATIC GAIN CONTROL
For simplicity of analysis
we drop the absolute value

## Slide 92
OTA-C CIRCUITS
Circuits created using capacitors, simulated resistors, adders and integrators
integrator
resistor
Frequency domain analysis assuming
ideal OTAs
Magnitude Bode plot

## Slide 93
LEARNING EXAMPLE
Two equations in three unknowns.
Select the capacitor value
OK

## Slide 94
TOW-THOMAS OTA-C BIQUAD FILTER
biquad ~ biquadratic

## Slide 95
LEARNING EXAMPLE
BW

## Slide 96
Bode plots for resulting amplifier

## Slide 97
LEARNING BY APPLICATION
Using a low-pass filter to reduce 60Hz ripple
Thevenin equivalent for AC/DC
converter
Using a capacitor to create a low-
pass filter
Design criterion: place the corner frequency
at least a decade lower

## Slide 98
Filtered output

## Slide 99
LEARNING EXAMPLE
Single stage tuned transistor amplifier
Select the capacitor for maximum
gain at 91.1MHz
Antenna
Voltage
Transistor
Parallel resonant circuit

## Slide 100
LEARNING BY DESIGN
Anti-aliasing filter
Nyquist Criterion
When digitizing an analog signal, such as music, any frequency components
greater than half the sampling rate will be distorted
In fact they may appear as spurious components. The phenomenon is known as
aliasing.
SOLUTION: Filter the signal before digitizing, and remove all components higher
than half the sampling rate. Such a filter is an anti-aliasing filter
For CD recording the industry standard is to sample at 44.1kHz.
An anti-aliasing filter will be a low-pass with cutoff frequency of 22.05kHz
Single-pole low-pass filter
Resulting magnitude Bode plot
Attenuation
in audio range

## Slide 101
Improved anti-aliasing filter
Two-stage buffered filter
One-stage
Two-stage
Four-stage

## Slide 102
Magnitude Bode plot
To design, pick one, e.g., C and determine the other
LEARNING BY DESIGN
Notch filter to eliminate 60Hz hum
Notch filter characteristic

## Slide 103
DESIGN EXAMPLE
ANTI ALIASING FILTER FOR MIXED MODE CIRCUITS
Visualization of aliasing
Signals of different
frequency and the same
samples
Ideally one wants to eliminate frequency components higher than twice the sampling frequency and make sure that all useful frequencies as properly sampled
Design specification
Simplifying assumption
Infinite input resistance (no load on RC circuit)
Design equation

## Slide 104
(non-inverting op-amp)
DESIGN EXAMPLE
“BASS-BOOST” AMPLIFIER
DESIRED BODE PLOT
OPEN SWITCH
(6dB)
Switch closed??

## Slide 105
DESIGN EXAMPLE
TREBLE BOOST
Original player response
Desired boost
Proposed boost circuit
Non-inverting amplifier
Design equations
Filters