## Slide 1: Chapter #5: MOSFET’s
from Microelectronic Circuits Text
by Sedra and Smith
Oxford Publishing
Speaker Notes by Jeffrey Denenberg, PhD – “DoctorD”
http://doctord.webhop.net
Notes: We are now discussing Metal-Oxide-Semiconductor Field Effect Transistors which are the prevalent technology in electronics today.

## Slide 2: Introduction
IN THIS CHAPTER WE WILL LEARN
  The physical structure of the MOS transistor and how it works.
  How the voltage between two terminals of the transistor control the current that flows through the third terminal, and the equations that describe these current-voltage characteristics.
  How the transistor can be used to make an amplifier, and how it can be used as a switch in digital circuits.

## Slide 3: Introduction
IN THIS CHAPTER WE WILL LEARN
  How to obtain linear amplification from the fundamentally nonlinear MOS transistor.
  The three basic ways for connecting a MOSFET to construct amplifiers with different properties.
  Practical circuits for MOS-transistor amplifiers that can be constructed using discrete components.

## Slide 4: Introduction
We have studied two-terminal semi-conductor devices (e.g. diode).
However, now we turn our attention to three-terminal devices.
They are more useful because they present multitude of applications, e.g:
    signal amplification, digital logic, memory, etc…

## Slide 5: Introduction
Q: What, in simplest terms, is the desired operation of a three-terminal device?
  A: Employ voltage between two terminals to control current flowing in to the third.
Notes: In England these are called “valves” due to the obvious analogy to fluid flow.

## Slide 6: Introduction
Q: What are two major types of three-terminal semiconductor devices?
  metal-oxide-semiconductor field-effect transistor (MOSFET)
  bipolar junction transistor (BJT)
Q: Why are MOSFET’s more widely used?
  size (smaller)
  ease of manufacture
  lesser power utilization
MOSFET technology
  It allows placement of approximately 2 billion transistors on a single IC
    backbone of very large scale integration (VLSI)
  It is considered preferable to BJT technology for many applications.
note: MOSFET are more widely used in implementation of modern electronic devices
note: This number is increasing exponentially as device size shrinks
Notes: Note that MOSFETs are the more recent development (1962) than Bipolar transistors (1947 – actually 1952 for the junction version). This is in spite of their operation being easier to understand.
Bipolar transistors were just beginning to be covered in EE curricula when I was in school (early 1960’s).
There was no mention of MOSFETS in that period.

## Slide 7: 5.1. Device Structure and Operation
Figure 5.1. shows general structure of the n-channel enhancement-type MOSFET
Figure 5.1: Physical structure of the enhancement-type NMOS transistor: (a) perspective view, (b) cross-section. Note that typically L = 0.03um to 1um, W = 0.1um to 100um, and the thickness of the oxide layer (tox) is in the range of 1 to 10nm.
Notes: Enhancement mode vs. Depletion Mode devices differ in their Gate voltage characteristics.
Enhancement – moving the gate voltage towards the drain voltage “enhances” channel conductance.
Depletion – moving the gate voltage away from the drain “depletes” carrier concentration in the channel.

## Slide 8: 5.1. Device Structure and Operation
Figure 5.1: Physical structure of the enhancement-type NMOS transistor: (a) perspective view, (b) cross-section. Note that typically L = 0.03um to 1um, W = 0.1um to 100um, and the thickness of the oxide layer (tox) is in the range of 1 to 10nm.
one p-type doped region
two n-type doped regions (drain, source)
layer of SiO2 separates source and drain
metal, placed on top of SiO2, forms gate electrode
Notes: The IC substrate (or “body) is “diode isolated” as both PN junctions are reverse biased.

## Slide 9: 5.1. Device Structure and Operation
The name MOSFET is derived from its physical structure.
However, many MOSFET’s do not actually use any “metal”, polysilicon is used instead.
  “This” has no effect on modeling / operation as described here.
Another name for MOSFET is insulated gate FET, or IGFET.
The device is composed of two pn-junctions, however they maintain reverse biasing at all times.
  Drain will always be at positive voltage with respect to source.
We will not consider conduction of current in this manner.
Notes: There are also Junction FETs (JFETs) which work by using a reverse biased pn-junction depletion region to affect channel conductance.

## Slide 10: 5.1.2. Operation with Zero Gate Voltage
With zero voltage applied to gate, two back-to-back diodes exist in series between drain and source.
“They” prevent current conduction from drain to source when a voltage vDS is applied.
  yielding very high resistance (1012ohms)
Figure 5.1: Physical structure…
Notes: These reverse biased diodes also isolate the MOSFET from the body of the silicon chip.

## Slide 11: 5.1.3. Creating a Channel for Current Flow
Q: What happens if (1) source and drain are grounded and (2) positive voltage is applied to gate? Refer to figure to right.
  step #1: vGS is applied to the gate terminal, causing a positive build up of positive charge along metal electrode.
  step #2: This “build up” causes free holes to be repelled from region of p-type substrate under gate.
Figure 5.2: The enhancement-type NMOS transistor with a positive voltage applied to the gate. An n channel is induced at the top of the substrate beneath the gate
Notes: We are interested in the “holes” since the body or substrate is p-type material (usually silicon) and holes are the majority carrier. The “induced” n-type channel is formed between the source and the drain by repelling the holes leaving the minority carriers (electrons) to conduct current.

## Slide 12: Q: What happens if (1) source and drain are grounded and (2) positive voltage is applied to gate? Refer to figure to right.
step #3: This “migration” results in the uncovering of negative bound charges, originally neutralized by the free holes
step #4: The positive gate voltage also attracts electrons from the n+ source and drain regions into the channel.
Figure 5.2: The enhancement-type NMOS transistor with a positive voltage applied to the gate. An n channel is induced at the top of the substrate beneath the gate
Notes: Negative charge concentration is “enhanced” by a positive voltage on the gate.
This creates an induced channel for current flow between the Drain and the Source n+ regions.
I am always bothered by the naming convention as current actually flows from the drain to the source. 

## Slide 13: Q: What happens if (1) source and drain are grounded and (2) positive voltage is applied to gate? Refer to figure to right.
step #5: Once a sufficient number of “these” electrons accumulate, an n-region is created…
  …connecting the source and drain regions
step #6: This provides path for current flow between D and S.
Figure 5.2: The enhancement-type NMOS transistor with a positive voltage applied to the gate. An n channel is induced at the top of the substrate beneath the gate
this induced channel is also known as an inversion layer
Notes: As I noted in the previous slide.

## Slide 14: 5.1.3. Creating a Channel for Current Flow
threshold voltage (Vt) – is the minimum value of vGS required to form a conducting channel between drain and source
  typically between 0.3 and 0.6Vdc
field-effect – when positive vGS is applied, an electric field develops between the gate electrode and induced n-channel – the conductivity of this channel is affected by the strength of field
  SiO2 layer acts as dielectric
effective / overdrive voltage – is the difference between vGS applied and Vt.
oxide capacitance (Cox) – is the capacitance of the parallel plate capacitor per unit gate area (F/m2)
Vtn is used for n-type MOSFET, Vtp is used for p-channel
Notes: SiO2 is glass! We have formed a parallel plate capacitor between the gate and the channel.

## Slide 15: 5.1.3. Creating a Channel for Current Flow
Q: What is main requirement for n-channel to form?
  A: The voltage across the “oxide” layer must exceed Vt.
For example, when vDS = 0…
  the voltage at every point along channel is zero
  the voltage across the oxide layer is uniform and equal to vGS
Q: How can one express the magnitude of electron charge contained in the channel?
  A: See below…
Q: What is effect of vOV on n-channel?
  A: As vOV grows, so does the depth of the n-channel as well as its conductivity.
Notes: The channel gets deeper and more conductive as Vgs exceeds Vt (remember that the “Over Voltage”, Vov = Vgs – Vt)

## Slide 16: 5.1.4. Applying a Small vDS
Q: For small values of vDS, how does one calculate iDS (aka. iD)? A: Equation (5.7)…
Q: What is the origin of this equation?
  A: Current is defined in terms of charge per unit length of n-channel as well as electron drift velocity.
Notes: W is the channel width defined by device geometry; L is, of course, the channel length

## Slide 17: 5.1.4. Applying a Small vDS
Q: How does one calculate charge per unit length of n-channel (Q/uL)?
  A: For small values of vDS, one can still assume that voltage between gate and n-channel is constant (along its length) – and equal to vGS.
  A: Therefore, effective voltage between gate and n-channel remains equal to vOV.
  A: Therefore, (5.2) from two slides back applies.

## Slide 18: 5.1.4. Applying a Small vDS
Q: How does one calculate charge per unit length of n-channel (Q/uL)?
  A: Use (5.2) to calculate charge per unit L of channel.
Q: How does one calculate electron drift velocity?
  A: Note that vDS establishes an electric field E across length of n-channel, this may calculate e-drift velocity.

## Slide 19: 5.1.4. Applying a Small vDS
Q: How does one calculate charge per unit length of n-channel (Q/uL)?
  A: Use (5.2) to calculate charge per unit L of channel.
Q: How does one calculate electron drift velocity?
  A: Note that vDS establishes an electric field E across length of n-channel, this may calculate e-drift velocity.
Note that these two values may be employed to define current in amperes (aka. C/s).

## Slide 20: 5.1.4. Applying a Small vDS
Q: What is observed from equation (5.7)?
  A: For small values of vDS, the n-channel acts like a variable resistance whose value is controlled by vOV.
Notes: MOSFETs biased in the in “triode” region (The name, Triode” comes from the similar characteristics to that of vacuum tube triodes) are voltage controlled resistors! This can be a useful functionality in some designs (e.g. Volume controls in audio equipment).

## Slide 21: 5.1.4. Applying a Small vDS
Q: What do we note from equation (5.7)?
  A: For small values of vDS, the n-channel acts like a variable resistance whose value is controlled by vOV.
Note that this vOV represents the depth of the n-channel - what if it is not assumed to be constant? How does this equation change?
Note that this is one VERY IMPORTANT equation in Chapter 5.

## Slide 22: 5.1.4. Applying a Small vDS
Q: What three factors is rDS dependent on?
  A: process transconductance parameter for NMOS (mnCox) – which is determined by the manufacturing process
  A: aspect ratio (W/L) – which is dependent on size requirements / allocations
  A: overdrive voltage (vOV) – which is applied by the user
Notes: Manufacturing process – ie the dopant concentrations of the substrate

## Slide 23
1/rDS
Figure 5.4: The iD-vDS characteristics of the MOSFET in Figure 5.3. when the voltage applied between drain and source VDS is kept small.
high resistance, low vOV
low resistance, high vOV
kn is known as NMOS-FET transconductance parameter and is defined as mnCoxW/L
Notes: Transconductance – parameter relates the input (gate voltage above threshold) to the conductance (drain to source)

## Slide 24: 5.1.5. Operation as vDS is Increased
Q: What happens to iD when vDS increases beyond “small values”?
  A: The relationship between them ceases to be linear.
Q: How can this non-linearity be explained?
  step #1: Assume that vGS is held constant at value greater than Vt.
  step #2: Also assume that vDS is applied and appears as voltage drop across n-channel.
  step #3: Note that voltage decreases from vGS at the source end of channel to vGD at drain end, where…
    vGD = vGS – vDS
    vGD = Vt + vOV – vDS
Notes: As you increase VDS to higher values the device moves towards “saturation” (the V-I graph rolls off towards horizontal)

## Slide 25
Figure 5.5: Operation of the e-NMOS transistor as vDS is increased.
avDS
avOV
The voltage differential between both sides of n-channel increases with vDS.
Notes: Note the trapezoidal shape of the n-channel

## Slide 26
Figure 5.6(a): For a MOSFET with vGS = Vt + vOV application of vDS causes the voltage drop along the channel to vary linearly, with an average value of vDS at the midpoint. Since vGD > Vt, the channel still exists at the drain end. (b) The channel shape corresponding to the situation in (a). While the depth of the channel at the source is still proportional to vOV, the drain end is not.
note the average value
note that we can define total charge stored in channel |Q| as area of this trapezoid
Notes: At some point, as we increase VDS, the channel depth at the drain gets to 0 and the device is fully saturated

## Slide 27: Q: How can this non-linearity be explained?
step #4: Define iDS in terms of vDS and vOV.
triode vs. saturation region
iD is dependent on the apparent vOV (not vDS inherently) which does not change after vDS > vOV
Notes: Triode Region – A vacuum tube Triode has the same characteristic curves as a MOSFET in this region.
The vacuum tube triode (AKA. a “valve” in England) was invented by Lee DeForest in 1907 which started the electronics age. Deforest called his invention the “Audion Tube” as it could amplify audio signals.
He was at Chicago’s Armour Institute (now the Illinois Institute of Technology, my Alma Mater) at that time.

## Slide 28
saturation occurs once vDS > vOV
Notes: This is a plot of ID vs VDS holding Vov constant.
Note that this graph and the formulas ignore the effect of pn junction depletion region width on the channel length.

## Slide 29: 5.1.6. Operation for vDS >> vOV
In section 5.1.5, we assume that n-channel is tapered but channel pinch-off does not occur.
  Trapezoid doesn’t become triangle for vGD > Vt
Q: What happens if vDS > vOV?
  A: MOSFET enters saturation region. Any further increase in vDS has no effect on iD.
Figure 5.8: Operation of MOSFET with vGS = Vt + vOV as vDS is increased to vOV. At the drain end, vGD decreases to Vt and the channel depth at the drain-end reduces to zero (pinch-off). At this point, the MOSFET enters saturation mode of operation. Further increasing vDS (beyond vOV) has no (sic) effect on the channel shape and iD remains constant.
pinch-off does not mean blockage of current
Notes: There is a small increase in ID as VDS moves further into saturation due to a small decrease in channel length.

## Slide 30: Example 5.1: NMOS MOSFET
Example 5.1. Problem Statement: Consider an NMOS process technology for which Lmin = 0.4mm, tox = 8nm, mn = 450cm2/Vs, Vt = 0.7V.
Q(a): Find Cox and k’n.
Q(b): For a MOSFET with W/L = 8mm/0.8mm, calculate the values of vOV, vGS, and vDSmin needed to operate the transistor in the saturation region with dc current ID = 100mA.
Q(c): For the device in (b), find the values of vOV and vGS required to cause the device to operate as a 1000ohm resistor for very small vDS.
Notes: I’ll leave the example for you to go over in the text. (pp. 243-244)

## Slide 31: 5.1.7. The p-Channel MOSFET
Figure 5.9(a) shows cross-sectional view of a p-channel enhancement-type MOSFET.
  structure is similar but “opposite” to n-channel
complementary devices – two devices such as the p-channel and n-channel MOSFET’s.
Figure 5.9(a): Physical structure of the PMOS transistor. Note that it is similar to the NMOS transistor shown in Figure 5.1(b), except that all semiconductor regions are reversed in polarity. (b) A negative voltage vGS of magnitude greater than |Vtp| induces a p-channel, and a negative vDS causes a current iD to flow from source to drain.
Notes: In a p-channel MOSFET everything is now backwards!
Mirror image (or “complementary”) devices such as n-channel and p-channel or later NPN and PNP can be useful as a design option.

## Slide 32: 5.1.7. The p-Channel MOSFET
Q: What are main differences between n-channel and p-channel?
  A: Negative (not positive) voltage applied to gate “closes” the channel
    allowing path for current flow
  A: Threshold voltage (previously represented as Vt) is represented as Vtp
    |vGS| > |Vtp| to close channel
Figure 5.9(a): Physical structure of the PMOS transistor. Note that it is similar to the NMOS transistor shown in Figure 5.1(b), except that all semiconductor regions are reversed in polarity. (b) A negative voltage vGS of magnitude greater than |Vtp| induces a p-channel, and a negative vDS causes a current iD to flow from source to drain.

## Slide 33: 5.1.7. The p-Channel MOSFET
Q: What are main differences between n-channel and p-channel?
  A: Process transconductance parameters are defined differently
    k’p = mpCox
    kp = mpCox(W/L)
  A: The rest, essentially, is the same, but with reverse polarity...
Figure 5.9(a): Physical structure of the PMOS transistor. Note that it is similar to the NMOS transistor shown in Figure 5.1(b), except that all semiconductor regions are reversed in polarity. (b) A negative voltage vGS of magnitude greater than |Vtp| induces a p-channel, and a negative vDS causes a current iD to flow from source to drain.

## Slide 34: 5.1.7. The p-Channel MOSFET
PMOS technology originally dominated the MOS field (over NMOS). However, as manufacturing difficulties associated with NMOS were solved, “they” took over
Q: Why is NMOS advantageous over PMOS?
  A: Because electron mobility mn is 2 – 4 times greater than hole mobility mp.
complementary MOS (CMOS) technology – is technology which allows fabrication of both N and PMOS transistors on a single chip.
Notes: CMOS:
first invented in 1963 at Fairchild Semiconductor
ICs first produced at RCA for digital watches
Now a dominant IC technology

## Slide 35: 5.1.8. Complementary MOS or CMOS
CMOS employs MOS transistors of both polarities.
  more difficult to fabricate
  more powerful and flexible
  now more prevalent than NMOS or PMOS
Figure 5.10: Cross-section of a CMOS integrated circuit. Note that the PMOS transistor is formed in a separate n-type region, known as an n well. Another arrangement is also possible in which an n-type body is used and the n device is formed in a p well. Not shown are the connections made to the p-type body and to the n well; the latter functions as the body terminal for the p-channel device.
Notes: CMOS was first demonstrated by RCA for watches (low power digital logic). RCA then owned the technology but frittered it away by a series of management errors. This is a recurring theme in the history of electronics.

## Slide 36
Figure 5.10: Cross-section of a CMOS integrated circuit. Note that the PMOS transistor is formed in a separate n-type region, known as an n well. Another arrangement is also possible in which an n-type body is used and the n device is formed in a p well. Not shown are the connections made to the p-type body and to the n well; the latter functions as the body terminal for the p-channel device.
p-type semiconductor provides the MOS body (and allows generation of n-channel)
n-well is added to allow generation of p-channel
SiO2 is used to isolate NMOS from PMOS
Notes: The diode between the PMOS n-well and the p-type substrate isolates the PMOS transistor. Note the need for a more complex sequence of diffusions.

## Slide 37: Quick Recap!
The equation used to define iD depends on relationship btw vDS and vOV.
  vDS << vOV
  vDS < vOV
  vDS => vOV
  vDS >> vOV
This has not been covered yet!
Notes: Same as for NMOS, but backwards

## Slide 38: 5.2. Current-Voltage Characteristics
Figure 5.11. shows an n-channel enhancement MOSFET.
There are four terminals:
  drain (D), gate (G), body (B), and source (S).
Although, it is assumed that body and source are connected.
Figure 5.11 (a): Circuit symbol for the n-channel enhancement-type MOSFET. (b) Modified circuit symbol with an arrowhead on the source terminal to distinguish it from the drain and to indicate device polarity (i.e., n channel). (c) Simplified circuit symbol to be used when the source is connected to the body or when the effect of the body on device operation is unimportant.
Notes: Note that there are several different circuit symbols used for MOSFETs. The symbol used for P-Channel MOSFETs in Multisim causes much confusion – be careful. The internal (usually) connection between the body and the source means that a MOSFET will NOT work upside down.

## Slide 39: 5.2. Current-Voltage Characteristics
Although MOSFET is symmetrical device, one often designates terminals as source and drain.
Q: How does one make this designation?
  A: By polarity of voltage applied.
Arrowheads designate “normal” direction of current flow
  Note that, in part (b), we designate current as DS.
  No need to place arrow with B.
Figure 5.11 (a): Circuit symbol for the n-channel enhancement-type MOSFET. (b) Modified circuit symbol with an arrowhead on the source terminal to distinguish it from the drain and to indicate device polarity (i.e., n channel). (c) Simplified circuit symbol to be used when the source is connected to the body or when the effect of the body on device operation is unimportant.
the potential at drain (vD) is always positive with respect to source (vS)
Notes: The “symmetry” is not quite true for commercially available devices due to connection from the substrate to the source. They do not work when upside down.

## Slide 40: 5.2.2. The iD-vDS Characteristics
Table 5.1. provides a compilation of the conditions and formulas for operation of NMOS transistor in three regions.
  cutoff
  triode
  saturation

## Slide 41: 5.2.2. The iD-vDS Characteristics
At top of table, it shows circuit consisting of NMOS transistor and two dc supplies (vDS, vGS)
This circuit is used to demonstrate iD-vDS characteristic
  1st set vGS to desired constant
  2nd vary vDS
Two curves are shown…
  vGS < Vtn
  vGS = Vtn + vOV

## Slide 42
Notes: Put a sticky at this page! (page 249)

## Slide 43
Figure 5.12: The relative levels of the terminal voltages of the enhancement NMOS transistor for operation in the triode region and in the saturation region.

## Slide 44
Figure 5.13: The iD – vDS characteristics for an enhancement-type NMOS transistor
as vGS increases, so do the (1) saturation current and (2) beginning of the saturation region
equation (5.14)
Notes: Add a “Load Line” to find the Quiescent point as we did in Chapter 4 for diodes.

## Slide 45: 5.2.2. The iD-vGS Characteristic
Q: When MOSFET’s are employed to design an amplifier, in what range will they be operated?
  A: saturation
In saturation, the drain current (iD) is…
  dependent on vGS
  independent of vDS
In effect, it becomes a voltage-controlled current source.
  This is key for amplification.
Figure 5.13: The iD – vDS characteristics for an enhancement-type NMOS transistor
Notes: Saturation mode yields a simple circuit model

## Slide 46: 5.2.2. The iD-vGS Characteristic
In effect, it becomes a voltage-controlled current source.
  This is key for amplification.
  Refer to (5.21).
Q: What is one problem with (5.21)?
  A: It is nonlinear w/ respect to vOV … however, this is not of concern now.
Figure 5.14: The iD-vGS characteristic of an NMOS transistor operating in the saturation region. The iD-vOV characteristic can be obtained by simply re-labeling the horizontal axis, that is, shifting the origin to the point vGS = Vtn.
Notes: Later we will do a small signal analysis to “linearize” this model

## Slide 47: 5.2.2. The iD-vGS Characteristic
The view of transistor as CVCS is exemplified in figure 5.15.
  This circuit is known as the large-signal equivalent circuit.
  Current source is ideal.
  Infinite output resistance represents independent, in saturation, of iD from vDS..
Figure 5.15: Large-signal equivalent-circuit model of an n-channel MOSFET operating in the saturation
note that, in this circuit, iD is completely independent of vDS (because no shunt resistor exists)
Notes: Here is our equivalent circuit of an NMOS Amplifier in saturation before switching to a small signal analysis

## Slide 48: Example 5.2: NMOS Transistor
Example 5.2. Problem Statement: Consider an NMOS transistor fabricated in an 0.18-mm process with L = 0.18mm and W = 2mm. The process technology is specified to have Cox = 8.6fF/mm2, mn = 450cm2/Vs, and Vtn = 0.5V.
Q(a): Find VGS and VDS that result in the MOSFET operating at the edge of saturation with ID = 100mA.
Q(b): If VGS is kept constant, find VDS that results in ID = 50mA.
Q(c): To investigate the use of the MOSFET as a linear amplifier, let it be operating in saturation with VDS = 0.3V. Find the change in iD resulting from vGS changing from 0.7V by +0.01V and -0.01V.
Notes: Again, I’m leaving the examples for you to go over yourself. See pp. 251 – 253 in our text.

## Slide 49: 5.2.4. Finite Output Resistance in Saturation
In previous section, we assume (in saturation) iD is independent of vDS.
Therefore, a change DvDS causes no change in iD.
  This implies that the incremental resistance RS is infinite.
  It is based on the idealization that, once the n-channel is pinched off, changes in vDS will have no effect on iD.
  The problem is that, in practice, this is not completely true.
Notes: The real world is never ideal.

## Slide 50: 5.2.4. Finite Output Resistance in Saturation
Q: What effect will increased vDS have on n-channel once pinch-off has occurred?
  A: It will cause the pinch-off point to move slightly away from the drain & create new depletion region.
  A: Voltage across the (now shorter) channel will remain at (vOV).
  A: However, the additional voltage applied at vDS will be seen across the “new” depletion region.

## Slide 51: 5.2.4. Finite Output Resistance in Saturation
Q: What effect will increased vDS have on n-channel once pinch-off has occurred?
  A: This voltage accelerates electrons as they reach the drain end, and sweep them across the “new” depletion region.
  A: However, at the same time, the length of the n-channel will decrease.
    Known as channel length modulation.
this is the most important point here
Notes: “Channel Length Modulation” (The shortening of L with higher VDS) can be modeled by a Norton resistance across the controlled current source

## Slide 52: 5.2.4. Finite Output Resistance in Saturation
Q: How do we account for “this effect” in iD?
  A: Refer to (5.23).
  A: Addition of finite output resistance (ro).
Figure 5.16: Increasing vDS beyond vDSsat causes the channel pinch-off point to move slightly away from the drain, thus reducing the effective channel length by DL
Figure 5.18: Large-Signal Equivalent Model of the n-channel MOSFET in saturation, incorporating the output resistance ro. The output resistance models the linear dependence of iD on vDS and is given by (5.23)
Notes: This is a simple improvement to our NMOS circuit model in saturation mode.

## Slide 53: 5.2.4. Finite Output Resistance in Saturation
Q: How is ro defined?
  step #1: Note that ro is the 1/slope of iD-vDS characteristic.
  step #2: Define relationship between iD and vDS using (5.23).
  step #3: Take derivative of this function.
  step #4: Use above to define ro.
Note that ro may be defined in terms of iD, where iD does not take in to account channel length modulation…

## Slide 54: 5.2.4. Finite Output Resistance in Saturation
Q: What is l?
  A: A device parameter with the units of V -1, the value of which depends on manufacturer’s design and manufacturing process.
    much larger for newer tech’s
Figure 5.17 demonstrates the effect of channel length modulation on vDS-iD curves
  In short, we can draw a straight line between VA and saturation.
Figure 5.17: Effect of vDS on iD in the saturation region. The MOSFET parameter VA depends on the process technology and, for a given process, is proportional to the channel length L.
Notes: If you have ever drawn pictures with a “vanishing point” to handle the fact that objects get smaller at a distance, you will recognize this construct to correctly draw the sloped i-v relationship in saturation.

## Slide 55: 5.2.5. Characteristics of the p-channel MOSFET
Characteristics of the p-channel MOSFET are similar to the n-channel, however with many signs reversed.
Please review section 5.2.5 from the text, with focus on table 5.2.
Notes: Table 5.2 on page 257 deserves another “sticky”.

## Slide 56: 5.3. MOSFET Circuits at DC
We move on to discuss how MOSFET’s behave in dc circuits.
We will neglect the effects of channel length modulation (assuming l = 0).
We will work in terms of overdrive voltage (vOV), which reduces need to distinguish between PMOS and NMOS.
DC
Notes: Remember that Vov is the difference between VGS and VT.

## Slide 57: Example 5.3: NMOS Transistor
Problem Statement: Design the circuit of Figure 5.21, that is, determine the values of RD and RS – so that the transistor operates at ID = 0.4mA and VD = +0.5V. The NMOS transistor has Vt = 0.7V, mnCox = 100mA/V2, L = 1mm, and W = 32mm. Neglect the channel-length modulation effect (i. e. assume that l = 0).
Figure 5.21: Circuit for Example 5.3.
Notes: See page 259

## Slide 58: Example 5.4:
Refer to textbook…
Notes: See p. 260

## Slide 59: Example 5.5: MOSFET
Problem Statement: Design the circuit in Figure 5.23 to establish a drain voltage of 0.1V. What is the effective resistance between drain and source at this operating point? Let Vtn = 1V and k’n(W/L) = 1mA/V2.
Figure 5.23: Circuit for Example 5.5.
Notes: See pp. 261-262

## Slide 60: Example 5.6: MOSFET
Problem Statement: Analyze the circuit shown in Figure 5.24(a) to determine the voltages at all nodes and the current through all branches. Let Vtn = 1V and k’n(W/L) = 1mA/V2. Neglect the channel-length modulation effect (i.e. assume l = 0).
Figure 5.24: (a) Circuit for Example 5.6. (b) The circuit with some of the analysis details shown.
Notes: See pp. 263-264

## Slide 61: Example 5.7: PMOS Transistor
Problem Statement: Design the circuit of Figure 5.25 so that transistor operates in saturation with ID = 0.5mA and VD = +3V. Let the enhancement-type PMOS transistor have Vtp = -1V and k’p(W/L) = 1mA/V2. Assume l = 0.
Q: What is the largest value that RD can have while maintaining saturation-region operation?
Figure 5.25: Circuit for Example 5.7.
Notes: See pp. 264-265

## Slide 62: Example 5.8: CMOS Transistor
Problem Statement: The NMOS and PMOS transistors in the circuit of Figure 5.26(a) are matched, with k’n(Wn/Ln) = k’p(Wp/Lp) = 1mA/V2 and Vtn = -Vtp = 1V. Assuming l = 0 for both devices.
Q: Find the drain currents iDN and iDP, as well as voltage vO for vI = 0V, +2.5V, and -2.5V.
Figure 5.26: Circuits for Example 5.8.
Notes: “Matched” means? Almost identical parameters. See pp. 266 – 267
Going over these examples in detail will help you in doing the homework assignments.

## Slide 63: 5.4.1. Obtaining a Voltage Amplifier
In section 1.5 of text, we learned that a voltage controlled current source (VCCS) can serve as transconductance amplifier.
  the following slides (with blue tint) are a review
Q: How can we translate current output to voltage?
  A: Measure voltage drop across load resistor.
Figure 5.27: (a) simple MOSFET amplifier with input vGS and output vDS
example of transconductance amplifier

## Slide 64: 5.4.2. Voltage Transfer Characteristic
voltage transfer characteristics (VTC) – plot of out voltage vs. input
three regions exist in VTC
  vGS < Vt  cut off FET
    vOV = vGS – Vt < 0
    ID = 0
    vDS ??? vOV
    vout = vDD
  Vt < vGS < vDS + Vt  saturation
    vOV = vGS – Vt > 0
    ID = ½ kn(vGS – Vt)2
    vDS >> vOV
    vout = VDD – IDRD
  vDS + Vt < vGS < VDD  triode
    vOV = vGS – Vt > 0
    ID = kn(vGS – Vt – vDS)vDS
    vDS > vOV
    vout = VDD – IDRD
Figure 5.27: (b) the voltage transfer characteristic (VTC) of the amplifier from previous slide

## Slide 65: 5.4.2. Voltage Transfer Characteristic
Q: What observations may be drawn?
  A: Cutoff FET represents transistor blocking, cutoff AMP represents vout = 0
  A: As vGS increases…
    vDS (effectively) decreases
    iD increases
    vout decreases nonlinearly
    gain (G) decreases
  A: Once vDS > vDD, all power is dissipated by resistor RD
Figure 5.27: (b) the voltage transfer characteristic (VTC) of the amplifier from previous slide
cutoff FET
cutoff AMP

## Slide 66: 5.4.2. Voltage Transfer Characteristic
Q: How do we define vDS in terms of vGS for saturation?
Figure 5.27: (b) the voltage transfer characteristic (VTC) of the amplifier from previous slide
Q: How do we define point B – boundary between saturation and triode regions?

## Slide 67: 5.4.3. Biasing the MOSFET to Obtain Linear Amplification
Q: How can we linearize VTC?
  A: Appropriate biasing technique
  A: Dc voltage vGS is selected to obtain operation at point Q on segment AB
Q: How do we choose vGS?
  A: Will discuss shortly…
Figure 5.28: biasing the MOSFET amplifier at point Q located on segment AB of VTC
This equation differs from (5.32) because it considers dc component only.
Notes: Here we start the discussion of choosing a “Quiescent Point”, “Q” Point, or “Operating Point” and then assuming small perturbations to linearize our circuit model.

## Slide 68: 5.4.3. Biasing the MOSFET to Obtain Linear Amplification
bias point / dc operating pt. (Q) – point of linearization for MOSFET
  Also known as quiescent point.
Q: How will Q help us?
  A: Because VTC is linear near Q, we may perform linear amplification of signal << Q
Figure 5.28: biasing the MOSFET amplifier at point Q located on segment AB of VTC

## Slide 69: 5.4.3: Biasing the MOSFET to Obtain Linear Amplification
bias point / dc operating pt. (Q) = point of linearization for MOSFET
  also known as quiescent point
Q: how will Q help us?
  because VTC is linear near Q, we may perform linear amplification of signal << Q
Figure 5.28: biasing the MOSFET amplifier at point Q located on segment AB of VTC
linear amplification around Q in saturation region
Notes: The gain is the slope of this curve at the Q-point

## Slide 70: 5.4.3. Biasing the MOSFET to Obtain Linear Amplification
Q: How is linear gain achieved?
  step #1: Bias MOSFET with dc voltage VGS as defined by (5.34)
  step #2: Superimpose amplifier input (vgs) upon VGS.
  step #3: Resultant vds should be linearly proportional to small-signal component vgs.

## Slide 71: Q: How is linear gain achieved?
Figure 5.29: The MOSFET amplifier with a small time-varying signal vgs(t) superimposed on the dc bias voltage vGS. The MOSFET operates on a short almost-linear segment of the VTC around the bias point Q and provides an output voltage vds = Avvgs
As long as vgs(t) is small, its effect on vDS(t) will be linear – facilitating linear amplification.
Notes: Note the graphical “reflection” of the input through the amplifier gain curve.
This works for both linear and non-linear devices.

## Slide 72: Q: How is linear gain achieved?
step #4: Note if vgs is small, output vds will be nearly linearly proportional to it.
  Slope will be constant.
Notes: The gain is the tangent of the gain curve which is almost linear at the mid point of the saturation region.

## Slide 73: 5.4.4. Small-Signal Voltage Gain
Q: What observations can be made about voltage gain?
  A: Gain is negative.
  A: Gain is proportional to:
    load resistance (RD)
    transistor conductance parameter (kn)
    overdrive voltage (vOV)
Notes: These are reasonable approximations for small signals

## Slide 74: 5.4.4. Small-Signal Gain
Equation (5.38) is another version of (5.37) which incorporates (5.17).
It demonstrates that gain is ratio of:
  voltage drop across RD
  half of over voltage

## Slide 75: 5.4.4. Small-Signal Gain
Q: How does (5.38) relate to physical devices?
  A: For modern CMOS technology, vOV is usually no less than 0.2V.
  A: This means that max achievable gain is approximately 10VDD.
This does not mean that output may be 10x supply (VDD).
For example, 0.13mm CMOS technology with VDD = 1.3V yields maximum gain of 13V/V.

## Slide 76: Example 5.9: MOSFET Amplifier
Problem Statement: Consider the amplifier circuit shown in Figure 5.29(a). The transistor is specified to have Vt = 0.4V, k’n = 0.4mA/V2, W/L = 10, and l = 0. Also, let VDD = 1.8V, RD = 17.5kOhms, and VGS = 0.6V.
Q(a): For vgs = 0 (and hence vds = 0), find VOV, ID, VDS, and Av.
Q(b): What is the maximum symmetrical signal swing allowed at the drain? Hence, find the maximum allowable amplitude of a sinusoidal vgs.
Figure 5.29:
Notes: See pp. 272 - 273

## Slide 77: 5.4.5. Determining the VTC via Graphical Analysis
Graphical method for determining VTC is shown in Figure 5.31
Rarely used in practice, b/c difficult to draw vi-relationship.
Based on observation that, for each value of vGS, circuit will operate at intersection of iD and vDS.
Figure 5.31: Graphical construction to determine the voltage transfer characteristic of the amplifier in Fig. 5.29(a).
note: that slope of load line is dependent on -1/RD
Notes: This was our ONLY method to find the “Q” point for tube circuits back in the 60’s
Now you have Multisim!

## Slide 78: 5.4.5. Determining the VTC via Graphical Analysis
point A – where vGS = Vt
point Q – where MOSFET may be biased for amplifier operation
  vGS = VGS, vDS = VDS
point B – where MOSFET leaves saturation / enters triode
point C – where MOSFET is deep in triode region and vGS = VDD
Points A (open) and C (closed) are suitable for switch applications
Point Q is suitable for amplifier applications

## Slide 79: 5.4.5. Determining the VTC via Graphical Analysis
Figure 5.32: Operation of the MOSFET in Figure 5.29(a) as a switch: (a) Open, corresponding to point A in Figure 5.31; (b) Closed, corresponding to point C in Figure 5.31. The closure resistance is approximately equal to rDS because VDS is usually very small.

## Slide 80: 5.4.6. Locating the Bias Point Q
bias point (Q) – is determined by value of vGS and load resistance RD.
Two considerations in deciding Q:
  Required gain.
  Allowable signal swing at output.
Notes: The bias point, Q, and the output signal swing determines the amplifier’s distortion due to the non-linearity of the gain curve.

## Slide 81: 5.4.6. Locating the Bias Point Q
Q: How is Q for VTC defined (assuming RD is fixed)?
  A: As point Q approaches B:
    gain increases
    maximum vgs swing decreases

## Slide 82: 5.4.6. Locating the Bias Point Q
Note that a trade-off between gain and linear range exists.
linear range is large
gain is low
gain is high
linear range is small
Notes: The real world is full of trade-offs.

## Slide 83: 5.4.6. Locating the Bias Point Q
To define load resistance RD, one should refer to the iD - vDS plane.
Two examples of RD are shown to right for illustration:
  Q2: too close to triode
    not enough legroom
  Q1: too close to VDD
    not enough headroom
Ideally, we want to be somewhere in the middle.
Figure 5.33: Two load lines and corresponding bias points. Bias point Q1 does not leave sufficient room for positive signal swing at the drain (too close to VDD). Bias point Q2 is too close to the boundary of the triode region and might not allow for sufficient negative signal swing.
The objective is to prevent vDS from “clipping” or entering triode region

## Slide 84: 5.5. Small-Signal Operation and Models
Previously it was stated that linear amplification may be obtained from MOSFET via…
  Operation in saturation region
  Utilization of small-input
This section will explore small-signal operation in detail
  Note the conceptual amplifier circuit to right
Figure 5.34: Conceptual circuit utilized to study the operation of the MOSFET as a small-signal amplifier.
dc bias voltage
output voltage
input voltage to be amplified
Notes: This is a Common-Source amplifier as the source terminal is at AC ground.

## Slide 85: 5.5.1. The DC Bias Point
Q: How is dc bias current ID defined?
Figure 5.34: Conceptual circuit utilized to study the operation of the MOSFET as a small-signal amplifier.

## Slide 86: 5.5.2. The Signal Current in the Drain Terminal
Q: What is effect of vgs on iD?
  step #1: Define vGS as in (5.42).
  step #2: Define iD, separate terms as function of VGS and vgs
Note that this differs from previous analyses - because of attempt to isolate the effect of vgs from VGS.

## Slide 87: Q: What is effect of vgs on iD?
step #3: Classify terms.
  dc bias current (ID).
  linear gain – is desirable.
  nonlinear distortion – is undesirable, because rep. distortion.
Note that to minimize nonlinear distortion, vgs should be kept small.
½knvgs2 << kn(VGS-Vt)vgs
vgs << 2(VGS-Vt)
vgs << 2vOV
Notes: Any non-linear distortion is undesirable, but also unavoidable. It can only be minimized.

## Slide 88: Q: What is effect of vgs on iD?
step #4: Adapt (5.43) for small-signal condition.
  If vgs << 2vOV , neglect distortion.

## Slide 89
Figure 5.35: Small-signal operation of the MOSFET amplifier.
Notes: Again, reflection shows how the amplifier produces gain.

## Slide 90: 5.5.3. The Voltage Gain
Q: How is voltage gain (Av) defined?
  step #1: Define vDS for circuit of Figure 5.34 using KVL.
Figure 5.34: Conceptual circuit utilized to study the operation of the MOSFET as a small-signal amplifier.

## Slide 91: Q: How is voltage gain (Av) defined?
step #2: Isolate vds component of vDS.
step #3: Solve for gain (Av).
Figure 5.34: Conceptual circuit utilized to study the operation of the MOSFET as a small-signal amplifier.

## Slide 92: 5.5.3. The Voltage Gain
Output signal is shifted from input by 180O.
Input signal vgs << 2(VGS – Vt).
Operation should remain in MOSFET saturation region
  vDS > vGS – Vt (legroom)
  vDS < VDD (headroom)
Figure 5.36: Total instantaneous voltage vGS and vDS for the circuit in Figure 5.34.
Notes: A “Common Source” amplifier is an inverting amplifier!

## Slide 93: 5.5.5. Small-Signal Equivalent Models
From signal POV, FET behaves as VCCS.
  Accepts vgs between gate and source
  Provides current (iD) at drain
  Input resistance is high
    b/c gate terminal draws iG = 0
  Output resistance is high
Figure 5.37: Small-signal models for the MOSFET: (a) neglecting the dependence of iD on vDS in saturation (the channel-length modulation effect) and (b) including the effect of channel length modulation
Notes: The next few slides are a summary of our results.

## Slide 94: 5.5.5. Small-Signal Equivalent Models
Figure 5.37: Small-signal models for the MOSFET: (a) neglecting the dependence of iD on vDS in saturation (the channel-length modulation effect) and (b) including the effect of channel length modulation
Note that this resistor (ro) takes on value 10kOhm to 1MOhm and represents channel-length modulation.

## Slide 95: More Observations
Model (b) is more accurate than model (a)
ro = VA / ID
Small signal parameters (gm, ro) both depend on dc bias point
If channel-length modulation is considered, (5.51) becomes (5.54).

## Slide 96: 5.5.6. The Transconductance gm
Observations from (5.47)
  gm is proportional to mn, Cox, ratio W/L, dc component VOV.
  MOSFET with short / wide channel provides maximum gain.
  Gain may be increased via VGS, but not without reducing allowable swing of vgs.

## Slide 97: 5.5.6: The Transconductance gm
Observations from (5.47)
  gm is proportional to square root of dc bias current (ID)
  For given ID, gm is proportional to (W/L)1/2
This behavior is sharp contrast to the bipolar junction transistor (BJT).
  For which, gm is proportional to gm alone (not size or geometry).
Notes: We see the BJT (NPN and PNP transistors) in chapter 6

## Slide 98: 5.5.6. The Transconductance gm
Q: How does MOSFET compare to BJT? Assume ID = 0.5mA, k’n = 120mA/V2.
  A: MOSFET gm = 0.35mA/V
    W/L = 1
  A: MOSFET gm = 3.5mA/V
    W/L = 100
  A: BJT gm = 20mA/V

## Slide 99: 5.5.6: The Transconductance gm
Figure 5.38 illustrates the relationship defined in (5.57).
Figure 5.38: The slope of the tangent at the bias point Q intersects the vOV axis at 1/2VOV. Thus gm = ID/(1/2VOV).

## Slide 100: 5.5.6: The Transconductance gm
In summary, there are three relationships for determining gm:
  (5.55), (5.56), and (5.57)
These relationships are dependent on three design parameters:
  W/L, VOV, ID

## Slide 101: Example 5.10: MOSFET Amplifier
Example 5.10 Problem Statement: Figure 5.39(a) shows a discrete common-source MOSFET amplifier utilizing a drain-to-gate resistance RG for biasing purposes. Such a biasing arrangement will be studied in Section 5.7. The input signal vI is coupled to the gate via a large capacitor, and the output signal at the drain is couppled to the load resistance RL via another large capacitor. The transistor has Vt = 1.5V, k’n(W/L) = 0.25mA/V2, and VA = 50V. Assume the coupling capacitors to be sufficiently large so as to act as short circuits at the signal-frequencies of interest.
Q: We wish to analyze this amplifier circuit to determine its (a) small-signal voltage gain, its (b) input resistance, and the largest allowable input signal.
Notes: Example 5.10 is on pp. 283-284

## Slide 102
Figure 5.39: Example 5.10 amplifier circuit.
note: capacitors block dc signals completely, but have no effect on small-signal
Notes: A Common-Source, capacitive coupled, Amplifier. The capacitors do not affect AC performance as long as their reactance is small compared to circuit resistances.

## Slide 103: 5.5.7. The T Equivalent-Circuit Model
Through circuit transformation, it is possible to develop alternative circuit models
T-Equivalent-Ckt Model is shown to right.
Figure 5.40: Development of the T equivalent-circuit model for the MOSFET. For simplicity, ro has been omitted; however, it may be added between D and S in the T model of (d).

## Slide 104: 5.5.7. The T Equivalent-Circuit Model
Figure 5.40: Development of the T equivalent-circuit model for the MOSFET. For simplicity, ro has been omitted; however, it may be added between D and S in the T model of (d).
Q: How is this model developed?
  step #1: Begin with small signal model (assume Ro=0).
  step #2: Place second current source in series with the first.
    Has no effect on circuit operation.

## Slide 105: Q: How is T Equivalent-Circuit Model developed?
Figure 5.40: Development of the T equivalent-circuit model for the MOSFET. For simplicity, ro has been omitted; however, it may be added between D and S in the T model of (d).
step #3: Create new node X, which connects gate and drain terminals
  b/c the two current sources are equal, ig = 0
step #4: replace initial current source with equivalent resistance.
  iDS = gmvgs = vgs/Rgs

## Slide 106
Figure 5.40: Development of the T equivalent-circuit model for the MOSFET. For simplicity, ro has been omitted; however, it may be added.
ro

## Slide 107
Notes: Table 5.3 is another summary deserving a “sticky”.
Always use the model that makes your circuit analysis simpler.

## Slide 108: Summary
The enhancement-type MOSFET is current the modt widely used semiconductor device. It is the basis of CMOS technology, which is the most popular IC fabrication technology at this time. CMOS provides both n-channel (NMOS) and p-channel (PMOS) transistors, which increases design flexibility. The minimum MOSFET channel length achievable with a given CMOS process is used to characterize the process
The overdrive voltage |VOV| = |VGS| - |Vt| is the key quantity that governs the operation of the MOSFET. For amplifier applications, the MOSFET must operate in the saturation region.

## Slide 109: Summary
In saturation, iD shows some linear dependence on vDS as a result of the change in channel length. This channel-length modulation phenomenon becomes more pronounced as L decreases. It is modeled by ascribing an output resistance ro = |VA|/ID to the MOSFET model. Although the effect of ro on the operation of discrete-circuit MOS amplifiers is small, that is not the case in IC amplifiers.
The essence of the use of MOSFET as an amplifier is that in saturation vGS controls iD in the manner of a voltage-controller current source. When the device is dc biased in the saturation region, a small-signal input (vgs) may be amplified linearly.

## Slide 110: Summary
In cases where a resistance is connected in series with the source lead of the MOSFET, the T model is the most conveinant to use.
The three basic configurations of the MOS amplifiers are shown in Figure 5.43.
The CS amplifier has an ideally infinite input resistance and reasonably high gain – but a rather high output resistance and limited frequency response. It is used to obtain most of the gain in a cascade amplifier.
Adding a resistance Rs in the source lead of the CS amplifier can lead to beneficial results.
Notes: Figure 5.43 is on page 292
Cascade is the connection of two amplifiers in series to get the product of their gains.
Rs is helpful in setting the bias point as well as providing feedback to control/linearize gain.

## Slide 111: Summary
The CG amplifier has a low input resistance and thus it alone has limited and specialized applications. However, its excellent high-frequency response makes it attractive in combination with the CS amplifier.
The source follow has (ideally) infinite input resistance, a voltage gain lower than but close to unity, and a low output resistance. It is employed as a voltage buffer and as the output stage of a multistage amplifier.
A key step in the design of transistor amplifiers is to bias the transistor to operate at an appropriate point in the saturation region.
Notes: Common Gate, in spite of it’s name, is not common, but by providing good isolation between input and output, allows stable operation at high frequencies.
The Source follower (AKA Common Drain) is a useful buffer amplifier