## Slide 1: Analog and Digital Filter Design Laplace transform and z transform
Miroslav Lutovac and Dejan Tosic

## Slide 2: Overview
Definition and concept of transforms
Laplace transform
Z transform
Transfer function
Analysis of systems by transform method
Example analysis

## Slide 3: What are transforms?
The term transform refers to a mathematical operation that takes a given function, called the original and returns a new function, referred to as the image
The transformation is often done by an integral or summation formula
Commonly used transforms are named after Laplace and Fourier

## Slide 4: Why transforms?
Transforms are used to change a complicated problem into a simpler one:
  The simpler problem is solved in the image domain
  By using the inverse transform we obtain the solution in the original domain
Examples:
  Laplace transform to solve a differential equation
  z transform to solve a difference equation

## Slide 5: Benefits of transforms
Examine nature of signals or sequences
Solve LTI systems by transforming differential or difference equations into algebraic equations

## Slide 6: Concept of transforms
Transforms are based on suitable mapping of
  functions representing signals or sequences into new (complex) functions that we call the images
  the set of differential and difference equations, describing systems under analysis, into algebraic equations in a new (complex) variable
We investigate signals and systems by investigating the images or complex equations in new (complex) variables

## Slide 7: Key properties
Uniqueness
Homogeneity
Additivity
Differentiating and differencing, the operation of differentiating or differencing maps into the algebraic operation of multiplication

## Slide 8: Laplace transform
as a tool for solving continuous-time linear time-invariant systems and electric circuits

## Slide 9: Laplace Transform
Laplace transform is useful as an analytical tool in the characterization, analysis, and study of LTI systems and electrical circuits
It plays an important role in analyzing causal systems specified by linear constant-coefficient differential equations

## Slide 10: Definition
Laplace transform X(s) of a causal signal x(t)
Inverse Laplace transform
The two functions x(t) and X(s) form a Laplace transform pair which is designated by x(t) ↔ X(s). The variable s is called a complex frequency variable.

## Slide 11: Laplace transform pairs

## Slide 12: Properties
Uniqueness
Homogeneity
Additivity
Differentiation
Convolution

## Slide 13: Transfer function of continuous-time systems
Relaxed LTI system described by linear constant-coefficients differential equation
H(s)
Transfer function

## Slide 14: Analysis of CTLTI systems by transform method
Consider a continuous-time linear time-invariant (CTLTI) system specified by its block diagram and assume zero initial conditions (the system is at rest) and find the response of the system (signals at all nodes) for an excitation applied at node 1

## Slide 15: Analysis procedure
Label nodes by integer numbers
Assume that signal at some node is y(t)
Assume that input is a known function of time x(t)
Write equations characterizing each block
Apply the Laplace transform to both sides of each equation
Solve the set of algebraic equations
Find transfer function by dividing Y(s) by X(s) assuming zero initial conditions
Find the inverse Laplace transform of Y(s) to obtain the response y(t)

## Slide 16: Analysis steps
4
5
6
7
8

## Slide 17: Z transform
as a tool for solving discrete-time linear time-invariant systems

## Slide 18: Z Transform
Z transform is useful as an analytical tool in the characterization, analysis, and study of discrete-time LTI systems
It plays an important role in analyzing causal systems specified by linear constant-coefficient difference equations

## Slide 19: Definition
Z transform X(z) of a causal sequence {x(n)}
Inverse z transform
The sequence {x(n)} and the function X(z) form a z transform pair which is designated by {x(n) } ↔ X(z). The variable z is called a complex variable.
 is a contour in the counterclockwise sense enclosing all the singularities of X(z)

## Slide 20: Z transform pairs

## Slide 21: Properties
Uniqueness
Homogeneity
Additivity
Shifting
Convolution

## Slide 22: Convolution
Convolution of two causal sequences is defined as

## Slide 23: Transfer function of discrete-time systems
Relaxed LTI system described by linear constant-coefficients difference equation
H(z)
Transfer function

## Slide 24: Analysis of DTLTI systems by transform method
Consider a discrete-time linear time-invariant (DTLTI) system specified by its block diagram and assume zero initial conditions (the system is at rest) and find the response of the system (signals at all nodes) for an excitation applied at node 1

## Slide 25: Analysis procedure
Label nodes by integer numbers
Assume that signal at some node is y(n)
Assume that input is a known sequence x(n)
Write equations characterizing each block
Apply the z transform to both sides of each equation
Solve the set of algebraic equations
Find transfer function by dividing Y(z) by X(z) assuming zero initial conditions
Find the inverse z transform of Y(z) to obtain the response y(n)

## Slide 26: Analysis steps
5
6
7
8
4

## Slide 27: Further reading
M. D. Lutovac, D. V. Tošić, B. L. Evans
Filter Design for Signal Processing Using MATLAB and Mathematica
Prentice Hall Upper Saddle River, New Jersey ISBN 0-201-36130-2, (c) 2001
http://kondor.etf.bg.ac.yu/~lutovac/