## Slide 1: Filter Approximation Theory
Butterworth, Chebyshev, and Elliptic Filters

## Slide 2: Approximation Polynomials
Every physically realizable circuit has a transfer function that is a rational polynomial in s
We want to determine classes of rational polynomials that approximate the “Ideal” low-pass filter response (high-pass band-pass and band-stop filters can be derived from a low pass design)
Four well known approximations are discussed here:
  Butterworth: Steven Butterworth,"On the Theory of Filter Amplifiers", Wireless Engineer (also called Experimental Wireless and the Radio Engineer), vol. 7, 1930, pp. 536-541
  Chebyshev: Pafnuty Lvovich Chebyshev (1821-1894) - Russia Cyrillic alphabet - Spelled many ways
  Elliptic Function: Wilhelm Cauer (1900-1945) - Germany U.S. patents 1,958,742 (1934), 1,989,545 (1935), 2,048,426 (1936)
  Bessel: Friedrich Wilhelm Bessel, 1784 - 1846

## Slide 3: Definitions
Let |H()|2 be the approximation to the ideal low-pass filter response |I()|2
Where c is the ideal filter cutoff frequency (it is normalized to one for convenience)
|I()|2
/c
1
1

## Slide 4: Definitions - 2
|H()|2 can be written as
Where F() is the “Characteristic Function” which attempts to approximate:
  This cannot be done with a finite order polynomial
   provides flexibility for the degree of error in the passband or stopband.
F()

1
1


## Slide 5: Filter Specification
|H()|2 must stay within the shaded region
Note that this is an incomplete specification. The phase response and transient response are also important and need to be appropriate for the filter application
|H()|2

1
1
Pass band
Stop band
Transition Region

## Slide 6: Butterworth
F() = n and  = 1 and
Characteristics
  Smooth transfer function (no ripple)
  Maximally flat and Linear phase (in the pass-band)
  Slow cutoff 
|H()|2
1


## Slide 7: Butterworth Continued
Pole locations in the s-plane at: 2n = -1 or  = (-1)(1/2n)
  Poles are equally spaced on the unit circle at =k/2n.
  H(s) only uses the n poles in the left half plane for stability.
  There are no zeros
n = 3

## Slide 8: Butterworth Filter |H(s)| for n=4
H(s) = 1/( s4 + 2.6131s3 + 3.4142s2 + 2.6131s + 1)

## Slide 9: Chebyshev – Type 1
F() = Tn() so
  T1() =  and Tn() = 2 Tn() – Tn-1()
Characteristics
  Controlled equiripple in the pass-band
  Sharper cutoff than Butterworth
  Non-linear phase (Group delay distortion) 
1

|H()|2

## Slide 10: Chebyshev |H(s)| for n=4, r=1 (Type 1)
H(s) = 0.2457/( s4 + 0.9528s3 + 1.4539s2 + 0.7426s + 0.2756)
Poles lie on an ellipse

## Slide 11: Elliptic Function
F() = Un() – the Jacobian elliptic function
S-Plane
  Poles approximately on an ellipse
  Zeros on the j-axis
Characteristics
  Separately controlled equiripple in the pass-band and stop-band
  Sharper cutoff than Chebyshev (optimal transition band)
  Non-linear phase (Group delay distortion) 
|H()|2
1


## Slide 12: Elliptic Function H(s) for n=4, rp=3, rs=50
H(s) = (0.0032s4 + 0.0595s2 + 0.1554)/( s4 + 0.5769s3 + 1.2227s2 + 0.4369s + 0.2195)

## Slide 13: Bessel Filter
Butterworth and Chebyshev filters with sharp cutoffs (high order) carry a penalty that is evident from the positions of their poles in the s plane. Bringing the poles closer to the j axis increases their Q, which degrades the filter's transient response. Overshoot or ringing at the response edges can result.
The Bessel filter represents a trade-off in the opposite direction from the Butterworth. The Bessel's poles lie on a locus further from the j axis. Transient response is improved, but at the expense of a less steep cutoff in the stop-band.

## Slide 14: Practical Filter Design
Use a tool to establish a prototype design
  MatLab is a great choice
  See http://doctord.webhop.net/courses/Topics/Matlab/index.htm for a Matlab tutorial by Dr. Bouzid Aliane; Chapter 5 is on filter design.
Check your design for ringing/overshoot.
  If detrimental, increase the filter order and redesign to exceed the frequency response specifications
  Move poles near the j-axis to the left to reduce their Q
  Check the resulting filter against your specifications
    Moving poles to the left will reduce ringing/overshoot, but degrade the transition region.