## Slide 1: Noise: An Introduction
Adapted from a presentation in: Transmission Systems for Communications, Bell Telephone Laboratories, 1970, Chapter 7

## Slide 2: Noise: An Introduction
What is noise?
Waveforms with incomplete information
  Analysis: how?
  What can we determine?
Example: sine waves of unknown phase
  Energy Spectral Density
  Probability distribution function: P(v)
  Probability density function: p(v)
  Averages
Common probability density functions
  Gaussian
  Exponential
Noise in the real-world
Noise Measurement
Energy and Power Spectral densities

## Slide 3: Background Material
Probability
  Discrete
  Continuous
The Frequency Domain
  Fourier Series
  Fourier Transform

## Slide 4: Noise
Definition
  Any undesired signal that interferes with the reproduction of a desired signal
Categories
  Deterministic: predictable, often periodic, noise often generated by machines
  Random: unpredictable noise, generated by a “stochastic” process in nature or by machines

## Slide 5: Random Noise
Unpredictable
  “Distribution” of values
  Frequency spectrum: distribution of energy (as a function of frequency)
We cannot know the details of the waveform only its “average” behavior

## Slide 6: Noise analysis Introduction: a sine wave of unknown phase
Single-frequency interference n(t) = A sin(nt + ) A and n are known, but  is not known
We cannot know its value at time “t”

## Slide 7: Energy Spectral Density
Here the “Energy Spectral Density” is just the magnitude squared of the Fourier transform of n(t)
since all of the energy is concentrated at n and each half of the energy is at ±  since the Fourier transform is based on the complex exponential not sine and cosine.

## Slide 8: Probability Distribution
The “distribution” of the ‘noise” values
  Consider the probability that at any time t the voltage is less than or equal to a particular value “v”
The probabilities at some values are easy
  P(-A) = 0
  P(A) = 1
  P(0) = ½
The actual equation is: P(vn) = ½ + (1/)arcsin(vn/A)
Shown for A=1

## Slide 9: Probability Distribution continued
The actual equation is: P(vn) = ½ + (1/)arcsin(v/A)
Note that the noise spends more time near the extremes and less time near zero. Think of a pendulum:
  It stops at the extremes and is moving slowly near them
  It move fastest at the bottom and therefore spends less time there.
Another useful function is the derivative of P(vn): the “Probability Density Function”, p(vn) (note the lower case p)
Shown for A=1

## Slide 10: Probability Density Function
The area under a portion of this curve is the probability that the voltage lies in that region.
This PDF is zero for |vn| > A

## Slide 11: Averages
Time Average of signals
“Ensemble” Average
  Assemble a large number of examples of the noise signal. (the set of all examples is the “ensemble”)
  At any particular time (t0) average the set of values of vn(t0)
  to get the “Expected Value” of vn
When the time and ensemble averages give the same value (they usually do), the noise process is said to be “Ergodic”

## Slide 12: Averages (2)
Now calculate the ensemble average of our sinusoidal “noise”
Which is obviously zero (odd symmetry, balance point, etc. as it should since this noise the has no DC component.)

## Slide 13: Averages (3)
E[vn] is also known as the “First Moment” of p(vn)
We can also calculate other important moments of p(vn). The “Second Central Moment” or “Variance” (2) is: Which for our sinusoidal noise is:

## Slide 14: Averages (4)
Integrating this requires “Integration by parts
0

## Slide 15: Averages (5)
Continuing
Which corresponds to the power of our sine wave noise
Note:  (without the “squared”) is called the “Standard Deviation” of the noise and corresponds to the RMS value of the noise

## Slide 16: Common Probability Density Functions: The Gaussian Distribution
Central Limit Theorem
The probability density function for a random variable that is the result of adding the effects of many small contributors tends to be Gaussian as the number of contributors gets large.

## Slide 17: Common Probability Density Functions: The Exponential Distribution
Occurs naturally in discrete “Poison Processes”
  Time between occurrences
    Telephone calls
    Packets

## Slide 18: Common Noise Signals
Thermal Noise
Shot Noise
1/f Noise
Impulse Noise

## Slide 19: Thermal Noise
From the Brownian motion of electrons in a resistive material.
pn(f) = kT is the power spectrum where:
    k = 1.3805 * 10-23 (Boltzmann’s constant) and
    T is the absolute temperature (°Kelvin)
This is a “white” noise (“flat” spectrum)
  From a color analogy
  White light has all colors at equal energy
The probability distribution is Gaussian

## Slide 20: Thermal Noise (2)
A more accurate model (Quantum Theory)
  Which corrects for the high frequency roll off (above 4000 GHz at room temperature)
The power in the noise is simply
  Pn = k*T*BW Watts or
  Pn = -174 + 10*log10(BW) in dBm (decibels relative to a milliwatt)
  Note: dB = 10*log10 (P/Pref ) = 20*log10 (V/Vref )

## Slide 21: Shot Noise
From the irregular flow of electrons
  Irms = 2*q*I*f where: q = 1.6 * 10-19 the charge on an electron
This noise is proportional to the signal level (not temperature)
It is also white (flat spectrum) and Gaussian

## Slide 22: 1/f Noise
Generated by:
  irregularities in semiconductor doping
  contact noise
  Models many naturally occurring signals
    “speech”
    Textured silhouettes (Mountains, clouds, rocky walls, forests, etc.)
pn(f) =A / f  (0.8 <  < 1.5)

## Slide 23: Impulse Noise
Random energy spikes, clicks and pops
  Common sources
    Lightning
    Vehicle ignition systems
  This is a white noise, but NOT Gaussian
    Adding multiple sources - more impulse noise
    An exception to the “Central Limit Theorem”

## Slide 24: Noise Measurement
The Human Ear
  Average Performance
  The Cochlea
  Hearing Loss
Noise Level
  A-Weighted
  C-Weighted

## Slide 25: Hearing Performance (an average, good, ear)
Frequency response is a function of sound level
0 dB here is the threshold of hearing
Higher intensities yield flatter response

## Slide 26: The Cochlea
A fluid-filled spiral vibration sensor
  Spatial filter:
    Low frequencies travel the full length
    High frequencies only affect the near end
  Cillia: hairs put out signals when moved
    Hearing damage occurs when these are injured
    Those at the near end are easily damaged (high frequency hearing loss)

## Slide 27: Noise Intensity Levels: The A- Weighted Filter
Corresponds to the sensitivity of the ear at the threshold of hearing; used to specify OSHA safety levels (dBA)

## Slide 28: An A-Weighting Filter
Below is an active filter that will accurately perform A-Weighting for sound measurements Thanks to: Rod Elliott at http://sound.westhost.com/project17.htm

## Slide 29: Noise Intensity Levels: The C- Weighted Filter
Corresponds to the sensitivity of the ear at normal listening levels; used to specify noise in telephone systems (dBC)

## Slide 30: Energy Spectral Density (ESD)

## Slide 31: Energy Spectral Density (ESD) and Linear Systems
Therefore the ESD of the output of a linear system is obtained by multiplying the ESD of the input by |H()|2
X()
Y() = X() H()
H()

## Slide 32: Power Spectral Density (PSD)
Functions that exist for all time have an infinite energy so we define power as:

## Slide 33: Power Spectral Density (PSD-2)
As before, the function in the integral is a density. This time it’s the PSD
Both the ESD and PSD functions are real and even functions